## Slide 1: Unit-4: Assembly Language Programming Basics PART-I: 8085 Instruction Set
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof. Swati R Sharma
Microprocessor and Interfacing
(MPI)
GTU # 3160712

## Slide 2: Subject Overview
Sr. No. | Unit | % Weightage
1 | Introduction to Microprocessor | 8%
2 | Microprocessor Architecture and Operations | 7%
3 | 8085 Microprocessor | 12%
4 | Assembly Language Programming Basics | 13%
5 | 8085 Assembly Language Programs | 12%
6 | Stack & Subroutines | 13%
7 | I/O Interfacing | 20%
8 | Advanced Microprocessors | 15%

## Slide 3

Looping
Topics to be covered
  Assembly Language Programming Basics
    Hierarchy of Languages
    Compilers and Assemblers
    Instructions and Machine Language
    Advantages of High-Level Languages
    Why to Learn Assembly Language?
  Assembly Language Programming Tools
  Classification of 8085 Instructions
    Based on Byte Size
    Based on Function

## Slide 4: Hierarchy of Languages

## Slide 5: Hierarchy of Languages
Assembly language is a low-level programming language designed for a specific type of processor.
Uses symbolic names to represent operations, registers and memory locations.
Hardware
Micro Program Control
Application Program
High Level Language
Assembly Language
Machine Language
Machine Independent
Machine Specific
High Level Language
Low Level Language
Native to a processor: executed directly by hardware
Instructions consist of binary code: 1s and 0s
1100 1011
1100 1110
0100 1111
MOV BL,05h
ADD CL
MUL BH

## Slide 6: Compilers and Assemblers

## Slide 7: Compilers and Assemblers
High Level Language
Assembly Language
Machine Language
Compiler
Compiler
Assembler
Compilers translate high-level programs to machine code
either directly, or Indirectly via an assembler
Assemblers translates assembly code to machine code

## Slide 8: Instructions and Machine Language

## Slide 9: Instructions and Machine Language
Each command of a program is called an instruction (it instructs the computer, what to do?).
Computers only deal with binary data, hence the instructions must be in binary format (0’s and 1’s).
Therefore, each Opcode is having unique bit pattern of (0’s and 1’s).

## Slide 10: Instruction Fields
Assembly language instructions usually are made up of several fields.
Each field specifies different information.
The major two fields are:
  Opcode: Operation code that specifies operation to be performed.
    Each operation has its unique opcode.
  Operands: Fields which specify, where to get the source and destination operands for the operation specified by the opcode.

## Slide 11: Instruction Fields
Opcode | Operand
MOV | Rd, Rs M, Rs R, M
Rd  Destination Register
Rs  Source Register
M  Memory

## Slide 12: Translating Languages
English: Sum of A and B
High-Level Language: A + B
Assembly Language:
MVI A,02
MVI B,03
ADD B
Machine Language:
1001 1011 0010
1001 1001 0011
1011 0011 0010
A statement in a high-level language is translated typically into several machine-level instructions

## Slide 13: Advantages of High-Level Languages

## Slide 14: Advantages of High-Level Languages
Program development is faster
  High-level statements: fewer instructions to code.
Program maintenance is easier
  As Higher Level Language contains fewer instruction code.
Programs are portable
  Contain few machine-dependent details.
  Can be used with little or no modifications on different machines.
  Compiler translates to the target machine language.

## Slide 15: Why to Learn Assembly Language?

## Slide 16: Why to Learn Assembly Language?
Accessibility to system hardware
  Assembly Language is useful for implementing system software.
  It is also useful for small embedded system applications.
Space and Time efficiency
  Understanding sources of program efficiency.
  Tuning program performance.
  Writing compact code.
It is helpful for
  Compiler writing
  Programming microcontrollers
  Device drivers
  System design
  Low-level numeric routines

## Slide 17: Why to Learn Assembly Language?
Writing assembly programs gives the computer designer, deep understanding of the instruction set and how to design.
To be able to write compilers for HLL (Higher Level Language), we need to be expert with the machine language. Assembly programming provides such experience.

## Slide 18: Assembly Language Programming Tools

## Slide 19: Assembly Language Programming Tools
Assembler
Linker
Debugger
Editor

## Slide 20: Assembler
An assembler is a program that converts programs written in assembly language into object files(machine language).
Popular assemblers have emerged over the years for the Intel family of processors. These include …
  TASM (Turbo Assembler from Borland).
  NASM (Net wide Assembler for both Windows and Linux), and
  GNU assembler distributed by the free software foundation.

## Slide 21: Linker
A linker program is required to produce executable files.
It combines program's object file created by the assembler with other object files and link libraries, to produces a single executable program.

## Slide 22: Assembly Language Programming Tools
A project may consist of multiple source files
Assembler translates each source file separately into an object file
Linker links all object files together with link libraries
Assemble and Link Process
Source
File
Source
File
Source
File
Assembler
Object
File
Assembler
Object
File
Assembler
Object
File
Linker
Executable
File
Link
Libraries

## Slide 23: Debugger
Allows you to trace the execution of a program.
Allows you to view code, memory, registers etc.
Example: WinDbg, GDB - the GNU debugger, etc.

## Slide 24: Editor
Allows to create assembly language source files.
Some editors provide syntax highlighting features and can be customized as per programming environment.

## Slide 25: Classification of 8085 Instructions

## Slide 26
Classification of 8085 Instructions
One-byte Instructions
Requires one memory location
to perform an operation
E.g. CMA, ADD
Two-byte Instructions
Requires two memory locations
to perform an operation
E.g. MVI A,32H
Three-byte Instructions
Requires three memory locations
to perform an operation
E.g. JMP, CALL
Based on Byte Size
Based on Function
Data Transfer Instructions
Arithmetic Instructions
Logic & Bit Manipulation
Instructions
Branch Instructions
Control Instructions

## Slide 27: Classification of 8085 instructions
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
Each instruction is represented by an 8-bit binary value called Op-Code.
The entire group of instructions that a microprocessor supports is known as an Instruction Set.

## Slide 28: Classification of 8085 instructions
Instruction Set
  It is the set of instructions that the microprocessor can understand.
Opcode
  Known as Operation Code.
  This required field contains the mnemonic operation code for the 8085 instruction.
Operand
  The operand field identifies the data to be operated on by the specified opcode.
  Some instructions require no operands, while others require one or two operands.
MVI D, 8BH
Opcode
Operand

## Slide 29: Classification of 8085 instructions
General Terms
R | 8085 8-bit register (A, B, C, D, E, H, L)
Rp | Register Pair (BC, DE, HL)
M | Memory
Rs | Register Source
Rd | Register Destination

## Slide 30: One-byte Instruction
Instruction |  | Binary Code | Hexa Code
Opcode | Operand |  | 
MOV | C,A | 0100 1111 | 4FH
ADD | B | 1000 0000 | 80H
CMA |  | 0010 1111 | 2FH
One-byte instructions includes Opcode and Operand in the same byte.

## Slide 31: List of one-byte Instructions
Sr. | Instruction | Sr. | Instruction | Sr. | Instruction | Sr. | Instruction
1 | MOV dest.,src | 13 | SBB R/M | 25 | RNZ | 37 | CMA
2 | LDAX RP (B/D) | 14 | INR R/M | 26 | RPE | 38 | CMC
3 | STAX RP | 15 | INX RP | 27 | RPO | 39 | STC
4 | XCHG | 16 | DCR R/M | 28 | RST 0-7 | 40 | NOP
5 | SPHL | 17 | DCX RP | 29 | CMP R/M | 41 | HLT
6 | XTHL | 18 | DAA | 30 | ANA R/M | 42 | DI
7 | PUSH RP | 19 | RET | 31 | XRA R/M | 43 | EI
8 | POP RP | 20 | RC | 32 | ORA R/M | 44 | RIM
9 | ADD R/M | 21 | RNC | 33 | RLC | 45 | SIM
10 | ADC R/M | 22 | RP | 34 | RRC |  | 
11 | DAD | 23 | RM | 35 | RAL |  | 
12 | SUB R/M | 24 | RZ | 36 | RAR |  | 

## Slide 32: Two-byte Instruction
Instruction |  | Binary Code | Hexa Code
Opcode | Operand |  | 
MVI | A,32H | 0011 1110 0011 0010 | 3E: 1st Byte 32: 2nd Byte
MVI | B,F2H | 0011 1110 1111 0010 | 3E: 1st Byte F2: 2nd Byte
IN | 0AH | 1101 1011 0000 1010 | DB: 1st Byte 0A: 2nd Byte
In two-byte instruction,
1st Byte : Specifies Opcode
2nd Byte: Specifies Operand

## Slide 33: List of two-byte Instructions
Sr. | Instruction
1 | MVI destination,8-bit data
2 | OUT 8-bit port address
3 | IN 8-bit port address
4 | ADI 8-bit data
5 | ACI 8-bit data
6 | SUI 8-bit data
7 | SBI 8-bit data
8 | CPI 8-bit data
9 | ANI 8-bit data
10 | XRI 8-bit data
11 | ORI 8-bit data

## Slide 34: Three-byte Instruction
Instruction |  | Binary Code | Hexa Code
Opcode | Operand |  | 
LDA | 2050H | 0011 1010 0101 0000 0010 0000 | 3A: 1st Byte 50: 2nd Byte 20: 3rd Byte
JMP | 2085H | 1100 0011 1000 0101 0010 0000 | C3: 1st Byte 85: 2nd Byte 20: 3rd Byte
In three-byte instruction,
1st Byte: Specifies Opcode
2nd Byte: Specifies lower order 8-bit address
3rd Byte: Specifies higher order 8-bit address

## Slide 35: List of three-byte Instructions
Sr. | Instruction | Sr. | Instruction
1 | LDA 16-bit address | 13 | JPE 16-bit address
2 | LXI Rp, 16-bit data | 14 | JPO 16-bit address
3 | LHLD 16-bit address | 15 | CALL 16-bit address
4 | STA 16-bit address | 16 | CC 16-bit address
5 | SHLD 16-bit address | 17 | CNC 16-bit address
6 | JMP 16-bit address | 18 | CP 16-bit address
7 | JC 16-bit address | 19 | CM 16-bit address
8 | JNC 16-bit address | 20 | CZ 16-bit address
9 | JP 16-bit address | 21 | CNZ 16-bit address
10 | JM 16-bit address | 22 | CPE 16-bit address
11 | JZ 16-bit address | 23 | CPO 16-bit address
12 | JNZ 16-bit address |  | 

## Slide 36: GTU Exam Questions
Sr | Questions | Marks | Year
1. | Explain the functions of following instructions of 8085 – state the bytes occupied, number of Machine cycle required and T-States 1. LXI H, 2050H 2. MOV B,A 3. STA 5050H 4. ADD C | 4 | W’18
2. | Explain the functions of following instructions of 8085 – state its number of bytes occupied, number of Machine cycle required and T-states. 1. MOV A,M 2. LXI H,1000H 3. DAA | 4 | S’19
3. | Explain One byte, Two byte, Three byte instruction. | 4 | W’19

## Slide 37
Classification of 8085 Instructions
One-byte Instructions
Requires one memory location
to perform an operation
E.g. CMA, ADD
Two-byte Instructions
Requires two memory locations
to perform an operation
E.g. MVI A,32H
Three-byte Instructions
Requires three memory locations
to perform an operation
E.g. JMP, CALL
Based on Byte Size
Based on Function
Data Transfer Instructions
Arithmetic Instructions
Logic & Bit Manipulation
Instructions
Branch Instructions
Control Instructions

## Slide 38: Data Transfer Instructions

## Slide 39: Data Transfer Instructions
Instructions copy data from source to destination.
While copying, the contents of source is not modified.
Data Transfer Instructions do not affect the flags.

## Slide 40: MOV: Move data from source to destination
Instruction |  | Description | Example
Opcode | Operand |  | 
MOV Rd, Rs MOV M, R MOV R, M | This instruction copies the contents of the source register into the destination register. Contents of the source register is not altered. If one of the operands is a memory, its location is specified by the contents of the HL registers. one-byte instruction. | MOV B, C ; BC MOV B, M;BM[HL] MOV M, B; M[HL]B

## Slide 41: MVI: Load 8-bit to Register/Memory
Instruction |  | Description | Example
Opcode | Operand |  | 
MVI R, Data M, Data | The 8-bit data is stored in the destination register or memory. If the operand is a memory location, its location is specified by the contents of the HL registers. Two-byte instruction. | MVI B, 57H; B12 MVI M, 12H ; M[HL]12

## Slide 42: Example: LDA Instruction
02
04
0A
06
0F
0D
05
03
A
B
C
D
E
H
L
Memory
Registers
LDA 2050H
2000
…
..
.
2049
2050
2051
2052
0D

## Slide 43: LDA: Load Accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
LDA 16-bit address | The contents of a memory location, specified by a 16-bit address in the operand, is copied to the accumulator. The contents of the source is not altered. Three-byte instruction. | LDA 2050H LDA 0006H

## Slide 44: LDAX: Load the accumulator indirect
Instruction |  | Description | Example
Opcode | Operand |  | 
LDAX Rp (B/D) | The contents of a memory location, specified by a 16-bit address in the operand, is copied to the accumulator. The contents of the source is not altered. | LDAX B ; AM[BC] LDAX D ; AM[DE]

## Slide 45: Example: LDAX Instruction
02
04
0A
06
0F
0D
05
03
00
06
A
B
C
D
E
H
L
Memory
Registers
LDAX B ; AM[BC]
0001
0002
0003
0004
0005
0006
0007
0008
0D

## Slide 46: LXI: Load the immediate register pair
Instruction |  | Description | Example
Opcode | Operand |  | 
LXI Rp, 16-bit Data | The instruction loads immediate 16-bit data into register pair. | 
34
A
B
D
H
L
Registers
LXI H, 2034H
20
Notes: This is a 3-byte instruction, the second byte
specifies the low-order address and the third
byte specifies the high-order address.

## Slide 47: STA: Store Accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
STA 16-bit address | The contents of accumulator is copied into the memory location specified by the operand. | STA 0002H
16-bit memory address
Notes: This is a 3-byte instruction, the second byte
specifies the low-order address and the third
byte specifies the high-order address.

## Slide 48: STAX: Store Accumulator Indirect
Instruction |  | Description | Example
Opcode | Operand |  | 
STAX Rp | The contents of accumulator is copied into memory location specified by the contents of the operand (register pair). The contents of the accumulator is not altered. | STAX B;M[BC]A
00
06
0D
A
B
C
D
E
H
L
Registers
02
04
0A
06
0F
05
03
Memory
0001
0002
0003
0004
0005
0006
0007
0008
0D
04
Notes: This is a 3-byte instruction, the second byte
specifies the low-order address and the third
byte specifies the high-order address.

## Slide 49: Example: LHLD Instruction
02
04
0A
06
0F
0D
05
03
A
B
C
D
E
H
L
Memory
Registers
LHLD 0006H
0001
0002
0003
0004
0005
0006
0007
0008
0D
05

## Slide 50: LHLD: Load H and L registers direct
Instruction |  | Description | Example
Opcode | Operand |  | 
LHLD 16-bit address | The instruction copies contents of the memory location pointed out by the address into register L and copies the contents of the next memory location into register H. The contents of source memory locations is not altered. | LHLD 2050H LHLD 0006H

## Slide 51: SHLD: Store H and L registers direct
Instruction |  | Description | Example
Opcode | Operand |  | 
SHLD 16-bit address | The contents of register L is stored in memory location specified by the 16-bit address in the operand and the contents of H register is stored into the next memory location by incrementing the operand. | SHLD 0002H
H
L
A2
D3
A2
D3
A2
D3
0001
0002
0003
0004
Memory

## Slide 52: XCHG: Exchange H and L with D and E
Instruction |  | Description | Example
Opcode | Operand |  | 
XCHG None | The contents of register H are exchanged with the contents of register D, and the contents of register L are exchanged with the contents of register E. | XCHG
A2
03
D3
08
D
E
H
L
D3
08
A2
03
D
E
H
L

## Slide 53: SPHL: Copy H and L registers to stack pointer
Instruction |  | Description | Example
Opcode | Operand |  | 
SPHL None | The instruction loads the contents of the H and L registers into the stack pointer register, the contents of H register provide the high-order address and the contents of L register provide the low-order address. The contents of the H and L registers are not altered. | SPHL
H
L
SP (16)
A2
D3
A2
D3

## Slide 54: XTHL: Exchange H and L with top of stack
Instruction |  | Description | Example
Opcode | Operand |  | 
XTHL None | The contents of L register is exchanged with stack location pointed out by contents SP. The contents of the H register are exchanged with the next stack location (SP+1). | XTHL
H
L
A2
D3
0001
0002
0003
0004
Memory
SP
SP
3F
2C
Registers

## Slide 55: Example: PUSH Instruction
23
06
40
06
40
A
B
C
D
E
H
L
SP
Memory
Registers
PUSH B
SP <- SP-1
SP <- B ;transfer high order bit to TOS
SP <- SP-1
SP <- C ;transfer low order bit to TOS
0008
0007
0006
0005
0004
0003
0002
0001
SP
SP

## Slide 56: PUSH: Push the register pair onto the stack
Instruction |  | Description | Example
Opcode | Operand |  | 
PUSH Rp | The contents of the register pair designated in the operand are copied onto the stack in the following sequence. The SP register is decremented and the contents of the high order register (B, D, H) are copied into that location. The SP register is decremented again and the contents of the low-order register (C, E, L) are copied to that location. | PUSH B

## Slide 57: Example: POP Instruction
03
06
40
06
40
A
B
C
D
E
H
L
SP
Memory
Registers
POP B
C <- SP ; transfer to low order bit from TOS
SP <- SP+1
B <- SP ; transfer to high order bit from TOS
SP <- SP+1
0008
0007
0006
0005
0004
0003
0002
0001
SP
SP

## Slide 58: POP: Pop off stack to the register pair
Instruction |  | Description | Example
Opcode | Operand |  | 
POP Rp | The contents of the memory location pointed out by the stack pointer register are copied to the low-order register (C, E, L) of the operand. The stack pointer is incremented by 1 and the contents of that memory location are copied to the high-order register (B, D, H) of the operand. The stack pointer register is again incremented by 1. | POP B

## Slide 59: OUT: Output from Accumulator to 8-bit port
Instruction |  | Description | Example
Opcode | Operand |  | 
OUT 8-bit port address | The contents of the accumulator are copied into the I/O port specified by the operand. | OUT 0AH

## Slide 60: IN: Input data to accumulator from with 8-bit port
Instruction |  | Description | Example
Opcode | Operand |  | 
IN 8-bit port address | The contents of the input port designated in the operand are read and loaded into the accumulator. | IN 0AH

## Slide 61
1 | MOV Dst,Src | Copy content | 1 Byte
2 | MVI (R/M), 8-bit Data | Load 8-bit to Register/Memory | 2 Byte
3 | LDA 16-bit address | Load Accumulator | 3 Byte
4 | LDAX Rp(B/D) | Load the accumulator indirect | 1 Byte
13 | PUSH Rp | Push the register pair onto the stack | 1 Byte
5 | LXI Rp, 16-bit Data | Load the register pair immediate | 3 Byte
6 | STA 16-bit address | Store Accumulator | 3 Byte
7 | STAX Rp | Store Accumulator Indirect | 1 Byte
8 | LHLD 16-bit address | Load H and L registers direct | 3 Byte
9 | SHLD 16-bit address | Store H and L registers direct | 3 Byte
10 | XCHG None | Exchange H and L with D and E | 1 Byte
11 | SPHL None | Copy H and L registers to the stack pointer | 1 Byte
12 | XTHL None | Exchange H and L with top of stack | 1 Byte
14 | POP Rp | Pop off stack to the register pair | 1 Byte
15 | OUT 8-bit port address | Output from Accumulator to 8-bit port address | 2 Byte
16 | IN 8-bit port address | Input data to accumulator from a port with 8-bit address | 2 Byte
Data Transfer Instructions

## Slide 62: GTU Exam Questions
Sr. | Questions | Marks | Year
1. | Explain the PUSH and POP instructions of the 8085 microprocessor with example. | 4 | W’17
2. | Explain the following instructions of the 8085 microprocessor with suitable example: STA, LDAX, XTHL | 7 | W’17
3. | Explain 8085 data transfer instructions with suitable examples. | 7 | S’18
4. | Define opcode and operand, and specify the opcode and the operand in the instruction MOV H, L | 3 | W’18
5. | Explain the following instructions of the 8085 microprocessor with suitable example: LHLD, SPHL, LDAX, XTHL | 4 | S’19
6. | The memory location 2070H holds the data byte F2H.Write instructions to transfer the data byte to the accumulator using three different opcodes: MOV, LDAX, and LDA. | 4 | W’19
7. | Register D contains 72H.Illustrate the instructions MOV and STAX to copy the contents of register B into memory location 8020H using indirect addressing. | 4 | W’19

## Slide 63
Classification of 8085 Instructions
One-byte Instructions
Requires one memory location
to perform an operation
E.g. CMA, ADD
Two-byte Instructions
Requires two memory locations
to perform an operation
E.g. MVI A,32H
Three-byte Instructions
Requires three memory locations
to perform an operation
E.g. JMP, CALL
Based on Byte Size
Based on Function
Data Transfer Instructions
Arithmetic Instructions
Logic & Bit Manipulation
Instructions
Branch Instructions
Control Instructions

## Slide 64: Arithmetic Instructions

## Slide 65
1 | ADD R/M | Add register or memory, to the accumulator | 1 Byte
13 | DCX Rp | Decrement register pair by 1 | 1 Byte
2 | ADC R/M | Add register to the accumulator with carry | 1 Byte
3 | ADI 8-bit data | Add the immediate to the accumulator | 2 Byte
4 | ACI 8-bit data | Add the immediate to the accumulator with carry | 2 Byte
5 | DAD Rp | Add the register pair to H and L registers | 1 Byte
6 | SUB R/M | Subtract the register/memory from accumulator | 1 Byte
7 | SBB R/M | Subtract the source and borrow from accumulator | 1 Byte
8 | SUI 8-bit data | Subtract the immediate from the accumulator | 2 Byte
9 | SBI 8-bit data | Subtract immediate from accumulator with borrow | 2 Byte
10 | INR R/M | Increment the register or the memory by 1 | 1 Byte
11 | INX Rp | Increment register pair by 1 | 1 Byte
12 | DCR R/M | Decrement the register or the memory by 1 | 1 Byte
14 | DAA | Decimal adjust accumulator | 1 Byte
Arithmetic Instructions

## Slide 66: ADD: Add register/memory to accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
ADD R/M | The contents of the operand (register or memory) are added to the contents of the accumulator and the result is stored in the accumulator. If the operand is a memory location, its location is specified by the contents of the HL registers. All flags are modified to reflect the result of the addition. | ADD B; A = A + B ADD M; A = A + M[HL]

## Slide 67: ADC: Add register to accumulator with carry
Instruction |  | Description | Example
Opcode | Operand |  | 
ADC R/M | The contents of the operand (register or memory) and the Carry flag are added to the contents of the accumulator and the result is stored in the accumulator. If the operand is a memory location, its location is specified by the contents of the HL registers. All flags are modified to reflect the result of the addition. | ADC B; A = A + B + CY ADC M; A = A + M[HL]+CY

## Slide 68: ADI: Add immediate 8-bit with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
ADI 8-bit data | The 8-bit data (operand) is added to the contents of the accumulator and the result is stored in the accumulator. All flags are modified to reflect the result of the addition. | ADI 03; A = A + 03h

## Slide 69: ACI: Add immediate 8-bit to accumulator with carry
Instruction |  | Description | Example
Opcode | Operand |  | 
ACI 8-bit data | The 8-bit data (operand) and the Carry flag are added to the contents of the accumulator and the result is stored in the accumulator. All flags are modified to reflect the result of the addition. | ACI 03; A = A + 03h + CY

## Slide 70: DAD: Add register pair to H and L registers
Instruction |  | Description | Example
Opcode | Operand |  | 
DAD Rp | The 16-bit contents of the specified register pair are added to the contents of the HL register and the sum is stored in the HL register. The contents of the source register pair are not altered. If the result is larger than 16 bits, the CY flag is set. No other flags are affected. | DAD B
Notes: DAD instruction adds the contents (16bit) of the specified register pair with that of HL pair. This instruction takes 10 T states including opcode fetch. The opcode fetch cycle takes 4 T states and the remaining 6 T states, divided into two machine cycles, are for the instruction execution. During these 6 T (two machine cycles) states no bus operations are performed. Hence they are called bus idle machine cycles. During this ALE, RD etc are not activated.

## Slide 71: DAD Instruction
02
08
02
03
A
B
C
D
E
H
L
Registers
02
08
02
03
+
04
0B
04
0B
02
03
DAD B

## Slide 72: SUB: Subtract register/memory from accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
SUB R/M | The contents of the operand (register or memory) is subtracted from the contents of the accumulator, and the result is stored in the accumulator. If the operand is a memory location, its location is specified by the contents of the HL registers. All flags are modified to reflect the result of the subtraction. | SUB B ; A=A-B SUB M ; A=A-M[HL]

## Slide 73: SBB: Subtract source & borrow from accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
SBB R/M | The contents of the operand (register or memory) and the Borrow flag are subtracted from the contents of the accumulator and the result is placed in the accumulator. If the operand is a memory location, its location is specified by the contents of the HL registers. All flags are modified to reflect the result of the subtraction. | SBB B; A=A - (B+CY) SBB M; A=A-(M[HL]+CY)

## Slide 74: SUI: Subtract immediate 8-bit from accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
SUI 8-bit data | The 8-bit data (operand) is subtracted from the contents of the accumulator and the result is stored in the accumulator. | SUI 08h; A = A - 08h

## Slide 75: SBI: Subtract immediate from accumulator with borrow
Instruction |  | Description | Example
Opcode | Operand |  | 
SBI 8-bit data | The 8-bit data (operand) and the borrow (CY) are subtracted from the contents of the accumulator and the result is stored in the accumulator. | SBI 08h; A=A - (08h+CY)

## Slide 76: INR: Increment register/memory by 1
Instruction |  | Description | Example
Opcode | Operand |  | 
INR R/M | The contents of the designated register or memory is incremented by 1 and the result is stored at the same place. If the operand is a memory location, its location is specified by the contents of the HL registers. | INR B;B=B+01 INR M;M[HL]=M[HL]+01

## Slide 77: INX: Increment register pair by 1
Instruction |  | Description | Example
Opcode | Operand |  | 
INX Rp | The contents of the designated register pair is incremented by 1 and the result is stored at the same place. | INX D; DE=DE+0001

## Slide 78: DCR: Decrement register/ memory by 1
Instruction |  | Description | Example
Opcode | Operand |  | 
DCR R/M | The contents of the designated register or memory is decremented by 1 and the result is stored in the same place. If the operand is a memory location, its location is specified by the contents of the HL registers. | DCR B;B=B-01 DCR M;M[HL]=M[HL]-01

## Slide 79: DCX: Decrement register pair by 1
Instruction |  | Description | Example
Opcode | Operand |  | 
DCX Rp | The contents of the designated register pair is decremented by 1 and their result is stored at the same place. | DCX B; BC=BC- 0001 DCX D; DE=DE- 0001

## Slide 80: DAA: Decimal Adjust Accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
DAA None | The contents of the accumulator is changed from a binary value to two 4-bit BCD digits. If the value of the low-order 4-bits in the accumulator is greater than 9 or if AC flag is set, the instruction adds 6 to the low-order four bits. If the value of the high-order 4-bits in the accumulator is greater than 9 or if the Carry flag is set, the instruction adds 6 to the high-order four bits. | DAA

## Slide 81: DAA Instruction
A
B
C
D
E
H
L
Registers
2A
0 0 1 0
1 0 1 0
+ 0 0 0 0 0 1 1 0
0
0
1
0
0
0
0
1
1
1
1
Valid BCD number
3 0

## Slide 82
1 | ADD R/M | Add register or memory, to the accumulator | 1 Byte
13 | DCX Rp | Decrement register pair by 1 | 1 Byte
2 | ADC R/M | Add register to the accumulator with carry | 1 Byte
3 | ADI 8-bit data | Add the immediate to the accumulator | 2 Byte
4 | ACI 8-bit data | Add the immediate to the accumulator with carry | 2 Byte
5 | DAD Rp | Add the register pair to H and L registers | 1 Byte
6 | SUB R/M | Subtract the register/memory from accumulator | 1 Byte
7 | SBB R/M | Subtract the source and borrow from accumulator | 1 Byte
8 | SUI 8-bit data | Subtract the immediate from the accumulator | 2 Byte
9 | SBI 8-bit data | Subtract immediate from accumulator with borrow | 2 Byte
10 | INR R/M | Increment the register or the memory by 1 | 1 Byte
11 | INX Rp | Increment register pair by 1 | 1 Byte
12 | DCR R/M | Decrement the register or the memory by 1 | 1 Byte
14 | DAA | Decimal adjust accumulator | 1 Byte
Arithmetic Instructions

## Slide 83
Classification of 8085 Instructions
One-byte Instructions
Requires one memory location
to perform an operation
E.g. CMA, ADD
Two-byte Instructions
Requires two memory locations
to perform an operation
E.g. MVI A,32H
Three-byte Instructions
Requires three memory locations
to perform an operation
E.g. JMP, CALL
Based on Byte Size
Based on Function
Data Transfer Instructions
Arithmetic Instructions
Logic & Bit Manipulation
Instructions
Branch Instructions
Control Instructions

## Slide 84: Branch Instructions

## Slide 85
Branch Instructions
1 | JMP | Jump unconditionally | 3 Byte
2 | JC | Jump on carry | 3 Byte
3 | JNC | Jump on no carry | 3 Byte
4 | JP | Jump on positive | 3 Byte
5 | JM | Jump on minus | 3 Byte
6 | JZ | Jump on zero | 3 Byte
7 | JNZ | Jump on no zero | 3 Byte
8 | JPE | Jump on parity even | 3 Byte
9 | JPO | Jump on parity odd | 3 Byte
10 | CALL | Call unconditionally | 3 Byte
11 | CC | Call on carry | 3 Byte
12 | CNC | Call on no carry | 3 Byte
13 | CP | Call on positive | 3 Byte
14 | CM | Call on minus | 3 Byte
15 | CZ | Call on zero | 3 Byte
16 | CNZ | Call on no zero | 3 Byte
17 | CPE | Call on parity even | 3 Byte
18 | CPO | Call on parity odd | 3 Byte
19 | RET | Return unconditionally | 1 Byte
20 | RC | Return on carry | 1 Byte
21 | RNC | Return on no carry | 1 Byte
22 | RP | Return on positive | 1 Byte
23 | RM | Return on minus | 1 Byte
24 | RZ | Return on zero | 1 Byte
25 | RNZ | Return on no zero | 1 Byte
26 | RPE | Return on parity even | 1 Byte
27 | RPO | Return on parity odd | 1 Byte
28 | PCHL | Load program counter with HL contents | 1 Byte
29 | RST | Restart | 1 Byte

## Slide 86: JMP: Jump unconditionally
Instruction |  | Description | Example
Opcode | Operand |  | 
JMP 16-bit address | The program sequence is transferred to the memory address given in the operand. | JMP 000AH

## Slide 87: JMP: Jump unconditionally
Memory Address | Instructions
0000H | MVI A,05
0002H | MOV B,A
0003H | MOV C,B
0004H | JMP 0009
0007H | ADI 02
0009H | SUB B
000AH | HLT
Memory Label | Instructions
 | MVI A,05
 | MOV B,A
 | MOV C,B
 | JMP L1
 | ADI 02
L1: | SUB B
 | HLT

## Slide 88: Branch Instruction
Instruction |  | Description | Example
Opcode | Operand |  | 
JC 16-bit address | Jump on Carry, Flag Status: CY=1 | JC 2030H
Jump Conditionally
JNC 16-bit address | Jump on No Carry, Flag Status: CY=0 | JNC 2030H
JZ 16-bit address | Jump on Zero, Flag Status: Z=1 | JZ 2030H
JNZ 16-bit address | Jump on No Zero, Flag Status: Z=0 | JNZ 2030H
JP 16-bit address | Jump on Positive, Flag Status: S=0 | JP 2030H
JM 16-bit address | Jump on Minus, Flag Status: S=1 | JM 2030H
JPE 16-bit address | Jump on Parity Even, Flag Status: P=1 | JPE 2030H
JPO 16-bit address | Jump on Parity Odd, Flag Status: P=0 | JPO 2030H

## Slide 89: RET: Return from subroutine unconditionally
Instruction |  | Description | Example
Opcode | Operand |  | 
RET | The program sequence is transferred from the subroutine to the calling program. | RET

## Slide 90: CALL: Call Unconditionally
Instruction |  | Description | Example
Opcode | Operand |  | 
CALL 16-bit address | Instruction transfers the program sequence to the memory address given in the operand. Before transferring, the address of the next instruction(PC) is pushed onto the stack. | CALL 000AH

## Slide 91: CALL: Call Unconditionally
Line | Instruction | Address | PC
1 | LXI H,1002 | [0000] | [0003]
2 | LXI D,3002 | [0003] | [0006]
3 | CALL ADD1 | [0006] | [0009]
4 | LXI B,4002 | [0009] | [000C]
5 | ADD1:MOV A,D | [000C] | [000D]
6 | ADD H | [000D] | [000E]
7 | RET | [000E] | 
05 | [2008]
 | [2007]
 | [2006]
 | [2005]
09
00
SP
SP
00
09
SP
SP

## Slide 92: Branch Instruction
Instruction |  | Description | Example
Opcode | Operand |  | 
CC 16-bit address | Call on Carry, Flag Status: CY=1 | CC 2030H
CALL Conditionally
CNC 16-bit address | Call on No Carry, Flag Status: CY=0 | CNC 2030H
CZ 16-bit address | Call on Zero, Flag Status: Z=1 | CZ 2030H
CNZ 16-bit address | Call on No Zero, Flag Status: Z=0 | CNZ 2030H
CP 16-bit address | Call on Positive, Flag Status: S=0 | CP 2030H
CM 16-bit address | Call on Minus, Flag Status: S=1 | CM 2030H
CPE 16-bit address | Call on Parity Even, Flag Status: P=1 | CPE 2030H
CPO 16-bit address | Call on Parity Odd, Flag Status: P=0 | CPO 2030H

## Slide 93: Branch Instruction
Instruction |  | Description | Example
Opcode | Operand |  | 
RC 16-bit address | Return on Carry, CY=1 | RC
Return from Subroutine
RNC 16-bit address | Return on No Carry, CY=0 | RNC
RZ 16-bit address | Return on Zero, Z=1 | RZ
RNZ 16-bit address | Return on No Zero, Z=0 | RNZ
RP 16-bit address | Return on Positive, S=0 | RP
RM 16-bit address | Return on Minus, S=1 | RP
RPE 16-bit address | Return on Parity Even, Flag Status: P=1 | RPE
RPO 16-bit address | Return on Parity Odd, Flag Status: P=0 | RPO

## Slide 94: PCHL: Load program counter with HL contents
Instruction |  | Description | Example
Opcode | Operand |  | 
PCHL None | The contents of registers H & L are copied into the program counter. The contents of H are placed as the high-order byte and the contents of L as the low-order byte. | PCHL

## Slide 95: RST: Restart
Instruction |  | Description | Example
Opcode | Operand |  | 
RST 0-7(N) | The RST instruction is used as software instructions in a program to transfer the program execution to one of the following eight locations. Instruction Restart Address RST 0 0000H RST 1 0008H RST 2 0010H RST 3 0018H RST 4 0020H RST 5 0028H RST 6 0030H RST 7 0038H | RST 5

## Slide 96: Branch Instruction
Instruction |  | Description | Example
Opcode | Operand |  | 
TRAP None | It restart from address 0024H | TRAP
The 8085 has additionally 4 interrupts, which can generate RST instructions internally and doesn’t require any external hardware.
RST 5.5 None | It restart from address 002CH | RST 5.5
RST 6.5 None | It restart from address 0034H | RST 6.5
RST 7.5 None | It restart from address 003CH | RST 7.5

## Slide 97
Branch Instructions
1 | JMP | Jump unconditionally | 3 Byte
2 | JC | Jump on carry | 3 Byte
3 | JNC | Jump on no carry | 3 Byte
4 | JP | Jump on positive | 3 Byte
5 | JM | Jump on minus | 3 Byte
6 | JZ | Jump on zero | 3 Byte
7 | JNZ | Jump on no zero | 3 Byte
8 | JPE | Jump on parity even | 3 Byte
9 | JPO | Jump on parity odd | 3 Byte
10 | CALL | Call unconditionally | 3 Byte
11 | CC | Call on carry | 3 Byte
12 | CNC | Call on no carry | 3 Byte
13 | CP | Call on positive | 3 Byte
14 | CM | Call on minus | 3 Byte
15 | CZ | Call on zero | 3 Byte
16 | CNZ | Call on no zero | 3 Byte
17 | CPE | Call on parity even | 3 Byte
18 | CPO | Call on parity odd | 3 Byte
19 | RET | Return unconditionally | 1 Byte
20 | RC | Return on carry | 1 Byte
21 | RNC | Return on no carry | 1 Byte
22 | RP | Return on positive | 1 Byte
23 | RM | Return on minus | 1 Byte
24 | RZ | Return on zero | 1 Byte
25 | RNZ | Return on no zero | 1 Byte
26 | RPE | Return on parity even | 1 Byte
27 | RPO | Return on parity odd | 1 Byte
28 | PCHL | Load program counter with HL contents | 1 Byte
29 | RST | Restart | 1 Byte

## Slide 98
Classification of 8085 Instructions
One-byte Instructions
Requires one memory location
to perform an operation
E.g. CMA, ADD
Two-byte Instructions
Requires two memory locations
to perform an operation
E.g. MVI A,32H
Three-byte Instructions
Requires three memory locations
to perform an operation
E.g. JMP, CALL
Based on Byte Size
Based on Function
Data Transfer Instructions
Arithmetic Instructions
Logic & Bit Manipulation
Instructions
Branch Instructions
Control Instructions

## Slide 99: Logical & Bit Manipulation Instructions

## Slide 100
Logical & Bit Manipulation Instructions
1 | CMP | Compare register or memory with accumulator | 1 Byte
2 | CPI | Compare immediate with accumulator | 2 Byte
3 | ANA | Logical AND register or memory with accumulator | 1 Byte
4 | ANI | Logical AND immediate with accumulator | 2 Byte
5 | XRA | Exclusive OR register or memory with accumulator | 1 Byte
6 | XRI | Exclusive OR immediate with accumulator | 2 Byte
7 | ORA | Logical OR register or memory with accumulator | 1 Byte
8 | ORI | Logical OR immediate with accumulator | 2 Byte
9 | RLC | Rotate accumulator left | 1 Byte
10 | RRC | Rotate accumulator right | 1 Byte
11 | RAL | Rotate accumulator left through carry | 1 Byte
12 | RAR | Rotate accumulator right through carry | 1 Byte
13 | CMA | Complement accumulator | 1 Byte
14 | CMC | Complement carry | 1 Byte
15 | STC | Set carry | 1 Byte

## Slide 101: CMP: Compare register/memory with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
CMP R/M | The contents of the operand (register or memory) is compared with the contents of the accumulator. Both contents are preserved. The result of the comparison is shown by setting the flags: if (A) < (reg/mem): carry flag is set(1). if (A) = (reg/mem): zero flag is set(1). if (A) > (reg/mem): carry and zero flags are reset(0). | CMP B CMP M

## Slide 102: CPI: Compare immediate with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
CPI 8-bit data | The second byte data is compared with the contents of the accumulator. The values being compared remain unchanged. The result of the comparison is shown by setting the flags: if (A) < data: carry flag is set(1). if (A) = data: zero flag is set(1). if (A) > data: carry and zero flags are reset(0). | CPI 89H

## Slide 103: ANA: AND register/memory with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
ANA R/M | The contents of the accumulator are logically ANDed with the contents of the operand (register or memory), and the result is placed in the accumulator. If the operand is a memory location, its address is specified by the contents of HL registers. S, Z, P are modified to reflect the result of the operation. CY is reset. AC is set. | ANA B ANA M

## Slide 104: ANI: AND immediate with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
ANI 8-bit data | The contents of the accumulator are logically ANDed with the 8-bit data (operand) and the result is placed in the accumulator. S, Z, P are modified to reflect the result of the operation. CY is reset. AC is set. | ANI 02H

## Slide 105: ORA: OR register/memory with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
ORA R/M | The contents of the accumulator is logically ORed with the contents of the operand (register or memory), and the result is placed in the accumulator. If the operand is a memory location, its address is specified by the contents of HL registers. S, Z, P are modified to reflect the result of the operation. CY and AC are reset. | ORA B ORA M

## Slide 106: ORI: OR immediate with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
ORI 8-bit data | The contents of the accumulator is logically ORed with the 8-bit data (operand) and the result is placed in the accumulator. S, Z, P are modified to reflect the result of the operation. CY is reset. AC is set. | ORI 02H

## Slide 107: XRA: Exclusive OR register/memory with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
XRA R/M | The contents of the accumulator is Exclusive ORed with the contents of the operand (register or memory), and the result is placed in the accumulator. If the operand is a memory location, its address is specified by the contents of HL registers. S, Z, P are modified to reflect the result of the operation. CY and AC are reset. | XRA B XRA M

## Slide 108: XRI: Exclusive OR immediate with accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
XRI 8-bit data | The contents of the accumulator are Exclusive Ored with the 8-bit data (operand) and the result is placed in the accumulator. S, Z, P are modified to reflect the result of the operation. CY is reset. AC is set. | XRI 02H

## Slide 109: RLC: Rotate accumulator left
Instruction |  | Description | Example
Opcode | Operand |  | 
RLC None | Each binary bit of the accumulator is rotated left by one position. Bit D7 is placed in the position of D0 as well as in the Carry flag(CY). CY is modified according to bit D7. S, Z, P, AC are not affected. | RLC

## Slide 110: Logical Instruction
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
RLC
0
1
0
1
0
0
0
1
CY
1
A:Accumulator
Rotate the accumulator left

## Slide 111: RRC: Rotate accumulator right
Instruction |  | Description | Example
Opcode | Operand |  | 
RRC None | Each binary bit of the accumulator is rotated right by one position. Bit D0 is placed in the position of D7 as well as in the Carry flag(CY). CY is modified according to bit D0. S, Z, P, AC are not affected. | RRC

## Slide 112: RRC: Example
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
CY
A:Accumulator
1
0
1
0
1
0
0
0
0
Rotate the accumulator right

## Slide 113: RAL: Rotate accumulator left through carry
Instruction |  | Description | Example
Opcode | Operand |  | 
RAL None | Each binary bit of the accumulator is rotated left by one position through the Carry flag. Bit D7 is placed in the Carry flag, and the Carry flag is placed in the least significant position D0. CY is modified according to bit D7. S, Z, P, AC are not affected. | RAL

## Slide 114: RAL: Example
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0
1
0
1
0
0
0
1
CY
A:Accumulator
Rotate the accumulator left through carry
0

## Slide 115: RAR: Rotate accumulator right through carry
Instruction |  | Description | Example
Opcode | Operand |  | 
RAR None | Each binary bit of the accumulator is rotated right by one position through the Carry flag. Bit D0 is placed in the Carry flag, and the Carry flag is placed in the most significant position D7. CY is modified according to bit D0. S, Z, P, AC are not affected. | RAR

## Slide 116: RAR: Example
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
CY
A:Accumulator
1
0
1
0
1
0
0
0
0
Rotate the accumulator right through carry
1

## Slide 117: CMA: Complement accumulator
Instruction |  | Description | Example
Opcode | Operand |  | 
CMA None | The contents of the accumulator are complemented. No flags are affected. | CMA
A
CMA
2A
0 0 1 0
1 0 1 0
1 1 0 1
0 1 0 1
D 5

## Slide 118: Logical Instruction
Instruction |  | Description | Example
Opcode | Operand |  | 
CMC None | The Carry flag is complemented. No other flags are affected. | CMC
CMC: Complement Carry
STC: Set Carry
Instruction |  | Description | Example
Opcode | Operand |  | 
STC None | The Carry flag is set(1). No other flags are affected. | STC

## Slide 119
Logical & Bit Manipulation Instructions
1 | CMP | Compare register or memory with accumulator | 1 Byte
2 | CPI | Compare immediate with accumulator | 2 Byte
3 | ANA | Logical AND register or memory with accumulator | 1 Byte
4 | ANI | Logical AND immediate with accumulator | 2 Byte
5 | XRA | Exclusive OR register or memory with accumulator | 1 Byte
6 | XRI | Exclusive OR immediate with accumulator | 2 Byte
7 | ORA | Logical OR register or memory with accumulator | 1 Byte
8 | ORI | Logical OR immediate with accumulator | 2 Byte
9 | RLC | Rotate accumulator left | 1 Byte
10 | RRC | Rotate accumulator right | 1 Byte
11 | RAL | Rotate accumulator left through carry | 1 Byte
12 | RAR | Rotate accumulator right through carry | 1 Byte
13 | CMA | Complement accumulator | 1 Byte
14 | CMC | Complement carry | 1 Byte
15 | STC | Set carry | 1 Byte

## Slide 120
Classification of 8085 Instructions
One-byte Instructions
Requires one memory location
to perform an operation
E.g. CMA, ADD
Two-byte Instructions
Requires two memory locations
to perform an operation
E.g. MVI A,32H
Three-byte Instructions
Requires three memory locations
to perform an operation
E.g. JMP, CALL
Based on Byte Size
Based on Function
Data Transfer Instructions
Arithmetic Instructions
Logic & Bit Manipulation
Instructions
Branch Instructions
Control Instructions

## Slide 121: Control Instructions

## Slide 122
Control Instructions
1 | NOP | No operation | 1 Byte
2 | HLT | Halt | 1 Byte
3 | DI | Disable interrupts | 1 Byte
4 | EI | Enable interrupts | 1 Byte
5 | RIM | Read interrupt mask | 1 Byte
6 | SIM | Set interrupt mask | 1 Byte

## Slide 123: Control Instructions
Instruction |  | Description | Example
Opcode | Operand |  | 
NOP None | No operation is performed. The instruction is fetched and decoded. However no operation is executed. It is used to increase processing time of execution. 1 CPU cycle is "wasted" to execute a NOP instruction. | NOP
HLT None | The CPU finishes executing the current instruction and stops further execution. An interrupt or reset is necessary to exit from the halt state. | HLT

## Slide 124: Control Instructions
Instruction |  | Description | Example
Opcode | Operand |  | 
DI None | Disable Interrupt The interrupt enable flip-flop is reset and all the interrupts except the TRAP are disabled. No flags are affected. | DI
EI None | Enable Interrupt The interrupt enable flip-flop is set and all interrupts are enabled. No flags are affected. This instruction is necessary to re enable the interrupts (except TRAP). | EI

## Slide 125: SIM: Set Interrupt Mask
Instruction |  | Description | Example
Opcode | Operand |  | 
SIM None | This is a multipurpose instruction used to : Set the status of interrupts 7.5, 6.5, 5.5 Set serial data input bit. The instruction loads eight bits in the accumulator with the following interpretations. | SIM

## Slide 126: SIM Instruction
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
A:Accumulator
M5.5
M6.5
M7.5
MSE
R7.5
X
SDE
SOD
To set mask for RST7.5,RST 6.5, RST5.5
Interrupt Masked if bit=1
Mask Set Enable: if 0, bits 0-2 are ignored
if 1, mask is set
Serial Output Data
It is used to transmit o/p bits.
Ignored if D6=0
Reset
RST 7.5 if D4=1
Serial Data Enable
If D6=1; bit D7 is output to SOD Latch

## Slide 127: SIM Instruction
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Accumulator
M5.5
M6.5
M7.5
MSE
R7.5
X
SDE
SOD
Example 1: MVI A,08H
SIM
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 128: RIM: Read Interrupt Mask
Instruction |  | Description | Example
Opcode | Operand |  | 
RIM None | This is a multipurpose instruction used to Read the status of interrupts 7.5, 6.5, 5.5 Read serial data input bit. It reads eight bits from accumulator with following interpretations. | RIM
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
A:Accumulator
5.5
6.5
7.5
IE
I5
I6
I7
SID
To read interrupt mask
Interrupt Masked if bit=1
Interrupt Enable Flag: 1=enable; 0=disable
To identify pending interrupts
1=pending interrupt
0=no pending interrupt
To receive
serial data

## Slide 129
Control Instructions
1 | NOP | No operation | 1 Byte
2 | HLT | Halt | 1 Byte
3 | DI | Disable interrupts | 1 Byte
4 | EI | Enable interrupts | 1 Byte
5 | RIM | Read interrupt mask | 1 Byte
6 | SIM | Set interrupt mask | 1 Byte

## Slide 130: GTU Exam Questions
Sr. | Questions | Marks | Year
1. | Explain the SIM and RIM instructions of the 8085 microprocessor. | 3 | S’19
2. | Explain the Functions of following instructions: RAL LDAX ADC | 3 | W’19
3. | Explain the Functions of following instructions: RLC LHLD SBB | 3 | W’19

## Slide 131: References
Book: | Microprocessor Architecture, Programming, and Applications with the 8085, Ramesh S. Gaonkar Pub: Penram International
Mobile Application | 8085 and 8086 Microprocessor Opcodes app from Play Store: http://tiny.cc/aopcodes

## Slide 132: Thank You