## Slide 1: Unit-4: Assembly Language Programming Basics PART-II: 8085 Assembly Program Basics
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof. Swati R Sharma
Microprocessor and Interfacing
(MPI)
GTU # 3160712

## Slide 2: Subject Overview
Sr. No. | Unit | % Weightage
1 | Introduction to Microprocessor | 8%
2 | Microprocessor Architecture and Operations | 7%
3 | 8085 Microprocessor | 12%
4 | Assembly Language Programming Basics | 13%
5 | 8085 Assembly Language Programs | 12%
6 | Stack & Subroutines | 13%
7 | I/O Interfacing | 20%
8 | Advanced Microprocessors | 15%

## Slide 3

Looping
Topics to be covered
  Addressing Modes in 8085
  8085 Assembly Language Programs Basics
  8085 Assembly Language Programs
    Writing & Assembling the Programs
    Executing the Programs
    Debugging the Programs
  T-States & Machine Cycle of 8085 Instructions
  Timing Diagram

## Slide 4: Addressing Modes in 8085

## Slide 5: Addressing Modes in 8085
Immediate Addressing Mode
Implicit Addressing Mode
Register Addressing Mode
Indirect Addressing Mode
Direct Addressing Mode

## Slide 6: Immediate Addressing Mode
8/16-bit data is specified in the instruction itself as one of its operand.
For example:
  MVI B,20H
  LXI D,1034H
  ADI 45H
  SUI 30H
  CPI 68H
Notes: ADI,ACI,SUI SBI,

## Slide 7: Direct Addressing Mode
8/16-bit memory address is directly provided with the instruction.
For example:
  LDA 1035H ; here 1035 is 16-bit memory address
  IN 02H ; 02 is 8-bit I/O port address
  OUT 03H ; 03 is 8-bit I/O port address

## Slide 8: Register Addressing Mode
It specifies register or register pair that contains data.
For example:
  MOV A,B ; A  B
  ADD B ; A  A+B
  DAD H ; HL  HL+RP

## Slide 9: Indirect Addressing Mode
In this type of addressing mode, the 16-bit memory address is indirectly provided with the instruction using a register pair.
For example:
  LDAX D; A <- M[DE]
  STAX B; A -> M[BC]

## Slide 10: Implicit/Implied Addressing Mode
This mode doesn’t require any operand; the data is specified by the Opcode itself.
For example:
  XTHL
  SPHL
  PCHL

## Slide 11: 8085 Assembly Language Programs Basics

## Slide 12: Writing Assembly Language Programs
Step-1: | Read the problem carefully.
Step-2: | Break it down into small steps.
Step-3: | Represent the sequence with flowchart.
Step-4: | Translate flowchart into appropriate mnemonic instructions.
Step-5: | Translate mnemonic into machine code.
Step-6: | Enter machine code in memory and execute.
Step-7: | Start troubleshooting-debugging a program
The steps to write Assembly Language Programs are as follows:

## Slide 13: Documentation
Appropriate comments are critical for conveying the logic behind the program.
The comment should explain what is intended; they should not explain mnemonics.
Comment is optional.
Example:
  MOV A,B ; Move data from B to A 
  MOV A,B ; send data to accumulator for processing 

## Slide 14: Program Execution
Machine code can be loaded in R/W memory, with reference to starting memory location.
Execution can be done in two ways:
  Execute entire code on click.
  Single step execution.
  It will execute one instruction at a time.
  We can observe the content of register and flag after execution of each instruction.

## Slide 15: Debugging Program
Debug a program is similar to troubleshooting hardware.
If the code doesn’t work, it is essential to search carefully for errors in programming logic, machine codes and execution.
How to Debug machine code:
Translating assembly to machine code is similar to building a circuit.
Following errors are common:
  Writing a wrong code.
  Specifying the wrong jump location.
  Writing memory address in decimal, thus specifying wrong jump location.
  Writing lower order and higher order bits in wrong sequence.

## Slide 16: 8085 Assembly Language Programs Basics

## Slide 17: 8085 Assembly Program: Add Two 8-bit Numbers
Write a program to add data at 1005H & 1006H memory location and store the result at 1007H memory location.
LXI H,1005 ; to retrive m/m addr
MOV A,M ; retrieve m/m content
INX H ; increment memeory to 1006H
ADD M ; add accumulator with M[1006]
STA 1007 ; store result
HLT ; HLT program
Start
End
Transfer 16-bit address to HL Pair
Data Transfer: A <- M[HL]
HL=HL + 1
A = A + M[HL]
Store result
[1007] <- A

## Slide 18: 8085 Assembly Program
Write a program to load register B with 37H and display number at the output Port 01
MVI B,37 ; B <- 37H
MOV A,B ; A <- B for I/O processing
OUT 01 ; PORT 01 <- A
HLT

## Slide 19: T-States & Machine Cycle of 8085 Instructions

## Slide 20: Timing Cycle required by 8085 Instructions
Operation | T-States
I/O Write | 3T
Opcode Fetch | 4-6T
Memory Read | 3T
Memory Write | 3T
I/O Read | 3T
Instruction that require 5T-States for Opcode Fetch
HLT
Instructions that require 6T-States for Opcode Fetch
    CALL
    Conditional CALL
    DCX
    INX
    PCHL
    SPHL
    PUSH
    Conditional RET

## Slide 21: Machine Cycle required by 8085 Instruction
Operation | M/C
I/O Write (IOW) | 1
Fetch (F) | 1
Memory Read (MEMR) | 1
Memory Write (MEMW) | 1
I/O Read (IOR) | 1
Read Immediate Data (R) | 1

## Slide 22: Timing and Machine Cycle
MOV B, D
Machine Cycle:
1(F) = 1 Machine Cycle
Timing Cycle:
= 4T (Fetch)

## Slide 23: Timing and Machine Cycle
2. MVI C ,17H
Machine Cycle: Fetch + R
1 + 1 = 2
Timing Cycle: Fetch + R
4T + 3T= 7T

## Slide 24: Timing and Machine Cycle
3. MVI M , 25H
Machine Cycle: Fetch + R+ Write data(MEMW)
1 + 1 + 1 = 3
Timing Cycle: Opcode Fetch + R + MEMW
4T + 3T + 3T = 10T

## Slide 25: Timing and Machine Cycle
4. MOV A,M
Machine Cycle: Fetch + Read Memory(MEMR)
1 + 1 = 2
Timing Cycle: Fetch + MEMR
4T + 3T = 7T

## Slide 26: Timing and Machine Cycle
4. MOV M, A
Machine Cycle: Fetch + Write Memory(MEMW)
1 + 1 = 2
Timing Cycle: Fetch + MEMW
4T + 3T = 7T

## Slide 27: Timing and Machine Cycle
5. NOP
Machine Cycle: Fetch
= 1 M/C Cycle
Timing Cycle: Fetch
= 4T

## Slide 28: Timing and Machine Cycle
6. HLT : Halt and enter wait state
Machine Cycle: Fetch + Wait
= 1 or more M/C Cycle
Timing Cycle: Fetch + Wait
= 5T or more T-States

## Slide 29: Timing and Machine Cycle
7. IN 18H
Machine Cycle: Fetch + R + IOR
= 1 + 1 + 1
= 3
Timing Cycle: Fetch + R + IOR
= 4T + 3T + 3T
= 10T

## Slide 30: Timing and Machine Cycle
8. OUT 19H
Machine Cycle: Fetch + R + IOW
= 1 + 1 + 1
= 3
Timing Cycle: Fetch + R + IOW
= 4T + 3T + 3T
= 10T

## Slide 31: Timing and Machine Cycle
9. ADD B
Machine Cycle: Fetch
= 1 Machine Cycle
Timing Cycle: Fetch
= 4T

## Slide 32: Timing and Machine Cycle
10. ADI 26H
Machine Cycle: Fetch + R
1 + 1 = 2
Timing Cycle: Fetch + MEMR
4T + 3T = 7T

## Slide 33: Timing and Machine Cycle
11. ADD M
Machine Cycle: Fetch + MEMR
1 + 1 = 2
Timing Cycle: Fetch + MEMR
4T + 3T = 7T

## Slide 34: Timing and Machine Cycle
12. SUB C
Machine Cycle: Fetch
= 1 Machine Cycle
Timing Cycle: Fetch
= 4T

## Slide 35: Timing and Machine Cycle
13. SUI 26H
Machine Cycle: Fetch + R
1 + 1 = 2
Timing Cycle: Fetch + MEMR
4T + 3T = 7T

## Slide 36: Timing and Machine Cycle
14. SUB M
Machine Cycle: Fetch + MEMR
1 + 1 = 2
Timing Cycle: Fetch + MEMR
4T + 3T = 7T

## Slide 37: Timing and Machine Cycle
15. LDA 2030H
Machine Cycle: Fetch + ReadL 8-bit + ReadH 8-bit +MEMR (content)
= 1 + 1 + 1 + 1
= 4
Timing Cycle: Fetch + MEMR + MEMR + MEMR
= 4T + 3T + 3T + 3T
= 13T

## Slide 38: Timing and Machine Cycle
16. POP RP : POP B
Machine Cycle: Fetch + MEMR (SP) + MEMR (SP+1)
= 1 + 1 + 1
= 3
Timing Cycle: Fetch + MEMR + MEMR
= 4T + 3T + 3T
= 10T

## Slide 39: Timing and Machine Cycle
16. PUSH RP : PUSH B
Machine Cycle: Fetch + MEMW (SP) + MEMW (SP-1)
= 1 + 1 + 1
= 3
Timing Cycle: Fetch + MEMW + MEMW
= 6T + 3T + 3T
= 12T

## Slide 40: LHLD Instruction
02
04
0A
06
0F
0D
05
03
A
B
C
D
E
H
L
Memory
Registers
LHLD 0006H
0001
0002
0003
0004
0005
0006
0007
0008
0D
05

## Slide 41: Timing and Machine Cycle
17. LHLD 2034H
Machine Cycle: Fetch + MEMRL (2034) + MEMRH (2034)
+ MEMR_Content (2034)
+ MEMR_Content (2035)
= 1 + 1 + 1 + 1 + 1
= 5
Timing Cycle: Opcode Fetch+ MEMR + MEMR + MEMR + MEMR
= 4T + 3T + 3T + 3T + 3T
= 16T

## Slide 42: Timing and Machine Cycle
18. RAR
Machine Cycle: Fetch
= 1 Machine Cycle
Timing Cycle: Fetch
= 4T

## Slide 43: Timing and Machine Cycle
19. XTHL
Machine Cycle: Fetch + MEMR(SP)+MEMW(L)+ MEMR(SP+1)+MEMW(H)
= 1 + 1 + 1 + 1 + 1
= 5
Timing Cycle: Fetch+ MEMR + MEMW + MEMR + MEMW
= 4T + 3T + 3T + 3T + 3T
= 16T

## Slide 44: Timing and Machine Cycle
20. CALL 2030H
Machine Cycle: Fetch + MEMWL(Store) + MEMWH(Store)
+ MEMRL(Call) + MEMRH(Call)
= 1 + 1 + 1 + 1 + 1
= 5
Timing Cycle: Fetch+ MEMW + MEMW + MEMR + MEMR
= 6T + 3T + 3T + 3T + 3T
= 18T

## Slide 45: Timing and Machine Cycle
21. RET
Machine Cycle: Fetch + MEMR (SP) + MEMR (SP+1)
= 1 + 1 + 1
= 3
Timing Cycle: Fetch + MEMR + MEMR
= 4T + 3T + 3T
= 10T

## Slide 46: Exercise: Find Byte Size, Timing & Machine Cycle
LDAX B
SHLD 2470
SPHL
DAA
INR R/M
JMP
PCHL
CMP R/M
RRC
RIM
SIM
ORA R/M
XCHG
DI
EI

## Slide 47: Exercise Solution
Sr. | Instruction | Byte Size | Machine Cycle | T-States
1. | LDAX B | 1 | F+R=2 | 4T+3T=7T
2. | SHLD 2470 | 3 | F+R+R+W+W=5 | 4T+3T+3T+3T+3T=16T
3. | SPHL | 1 | F=1 | 6T
4. | DAA | 1 | F=1 | 4T
5. | INR R INR M | 1 1 | F=1 F+R+W=3 | 4T 4T+3T+3T=10T
6. | JMP 2030 | 3 | F+R+R=3 | 4T+3T+3T=10T
7. | PCHL | 1 | F=1 | 6T
8. | CMP R CMP M | 1 1 | F=1 F+R=2 | 4T 4T+3T=7T
9. | RRC | 1 | F=1 | 4T
10. | RIM | 1 | F=1 | 4T

## Slide 48: Exercise Solution
Sr. | Instruction | Byte Size | Machine Cycle | T-States
11. | SIM | 1 | F=1 | 4T
12. | ORA R ORA M | 1 1 | F=1 F+R=2 | 4T 4T+3T=7T
13. | XCHG | 1 | F=1 | 4T
14. | DI | 1 | F=1 | 4T
15. | EI | 1 | F=1 | 4T

## Slide 49: Timing Diagram

## Slide 50
 | T1 | T2 | T3 | T4
High order memory address
Unspecified
Low order M/m addr.
Opcode
CLK
A8
AD0
AD7
ALE
IO/M
RD
A15
Opcode Fetch

## Slide 51
 | T1 | T2 | T3 | T4
High order memory address
Low order M/m addr.
Data from memory
CLK
A8
AD0
AD7
ALE
IO/M
RD
A15
Memory read cycle
S1 | S0 | Mode
0 | 0 | HLT
0 | 1 | WRITE
1 | 0 | READ
IO/M=0, S1=1 , S0=0
S1
S0

## Slide 52
 | T1 | T2 | T3 | T4
High order memory address
Low order M/m addr.
Data from Microprocessor
CLK
A8
AD0
AD7
ALE
IO/M
WR
A15
Memory write cycle
S1 | S0 | Mode
0 | 0 | HLT
0 | 1 | WRITE
1 | 0 | READ
IO/M=0, S1=0 , S0=1
S0
S1

## Slide 53
 | T1 | T2 | T3 | T4
High order I/O address
Low order I/O addr.
I/O data
CLK
A8
AD0
AD7
ALE
IOR
A15
I/O read cycle
S1 | S0 | Mode
0 | 0 | HLT
0 | 1 | WRITE
1 | 0 | READ
IO/M=1, S1=1 , S0=0
IO/M
S1
S0

## Slide 54
 | T1 | T2 | T3 | T4
High order I/O address
Low order I/O addr.
Data from Microprocessor
CLK
A8
AD0
AD7
ALE
IOW
A15
I/O write cycle
S1 | S0 | Mode
0 | 0 | HLT
0 | 1 | WRITE
1 | 0 | READ
IO/M=1, S1=0 , S0=1
IO/M
S0
S1

## Slide 55
Timing Diagram : MOV B,M
 | T1 | T2 | T3 | T4 | T5 | T6 | T7
CLK
A8
AD0
AD7
ALE
IO/M
A15
High order memory address
Unspecified
High order memory address
Low order M/m addr.
Opcode
Low order M/m addr.
Data from memory
RD
Opcode Fetch
Memory Read

## Slide 56
Timing Diagram : MVI A, 32H
 | T1 | T2 | T3 | T4 | T5 | T6 | T7
CLK
A8
AD0
AD7
ALE
IO/M
A15
High order memory address
Unspecified
High order memory address
Low order M/m addr.
Opcode
Low order M/m addr.
Read Immediate
RD
Opcode Fetch
Memory Read

## Slide 57: Calculate Execution time of MVI A,32H
Given: Clock Frequency (f) = 2 MHz
Calculation:
Step-1: T-state = clock period = = = 0.5 sec
Step-2: Execution time for Opcode Fetch
= 4T x 0.5 = 2sec
Step-3: Execution time for Memory Read
= 3T x 0.5 = 1.5sec
Step-4: Execution time for Instruction
= (4T + 3T) x 0.5
= 7T x 0.5
= 3.5sec

## Slide 58
Timing Diagram : OUT 02H
Opcode Fetch
Memory Read
 | T1 | T2 | T3 | T4 | T1 | T2 | T3 | T1 | T2 | T3
CLK
A8
AD0
AD7
ALE
IO/M
A15
High order
memory address
High order memory address
Unspecified
Port address 02H
RD
IOW
Low addr
02H
Low addr
Opcode
Port addr
Acc. content
I/O Write

## Slide 59
Timing Diagram : IN 02H
Opcode Fetch
Memory Read
 | T1 | T2 | T3 | T4 | T1 | T2 | T3 | T1 | T2 | T3
CLK
A8
AD0
AD7
ALE
IO/M
A15
High order memory address
High order memory address
Unspecified
Port address 02H
RD
IOR
Low addr
02H
Low addr
Opcode
Port addr
Acc. content
I/O Read

## Slide 60: GTU Exam Questions
Sr. | Questions | Marks | Year
1. | Draw the timing diagram of following instruction of the 8085 microprocessor. OUT 50h MOV A, B MVI A, 8bit | 7 | W’17 W’18 S’18 S’19
2. | How many machine cycles are executed by 8085 microprocessor? List down it. | 1 | S’18
3. | Explain various addressing modes of 8085 microprocessor. | 7 | S’18 W’18 W’19
4. | Identify the machine cycles in the following instructions 1. SUB B 2. ADI 47H 3. STA 2050H 4. PUSH B | 7 | W’18

## Slide 61: References
Book: | Microprocessor Architecture, Programming, and Applications with the 8085, Ramesh S. Gaonkar Pub: Penram International
Mobile Application | 8085 and 8086 Microprocessor Opcodes app from Play Store: http://tiny.cc/aopcodes

## Slide 62: Thank You