## Slide 1: Unit-3: 8085 Microprocessor
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof. Swati R Sharma
Microprocessor and Interfacing
(MPI)
GTU # 3160712

## Slide 2: Subject Overview
Sr. No. | Unit | % Weightage
1 | Introduction to Microprocessor | 8%
2 | Microprocessor Architecture and Operations | 7%
3 | 8085 Microprocessor | 12%
4 | Assembly Language Programming Basics | 13%
5 | 8085 Assembly Language Programs | 12%
6 | Stack & Subroutines | 13%
7 | I/O Interfacing | 20%
8 | Advanced Microprocessors | 15%

## Slide 3

Looping
Topics to be covered
  Introduction to 8085
  8085 Programming Model
  Bus Organization of 8085
  8085 pin diagram
  8085 Architecture/Block Diagram
  T-States, Machine and Instruction Cycle
  Demultiplexing Address and Data Bus AD0-AD7
  Timing Diagram
  Memory Interfacing
  Generating Control Signals

## Slide 4: Introduction to 8085

## Slide 5: Introduction to 8085
8085 is pronounced as "eighty-eighty-five" microprocessor.
It is an 8-bit microprocessor designed by Intel in 1977 using NMOS technology.
Notes: N-type metal-oxide-semiconductor logic

## Slide 6: Introduction to 8085
8 bit General purpose microprocessor (i.e. 8 bit data bus).
It is a single chip N MOS device with 40 pins.
It has multiplexed address and data bus.(AD0 - AD7).
It works on 5-Volt DC power supply.
The maximum clock frequency is 3MHz while minimum frequency is 500kHz.
It provides 16 address lines, therefore capable of addressing 216= 64K of memory.
It supports external interrupt request.
It has two 16 bit registers named program counters (PC) and stack pointer (SP).
Notes: A NPN transistor has electrons as majority charge carriers whereas the PNP transistor has holes as majority charge carrier. The mobility of electrons is better than mobility of holes. So a NPN transistor is faster in operation than a PNP transistor.

## Slide 7: Introduction to 8085
It generates 8 bit I/O address so it can access 28 = 256 input ports.
It provides 5 hardware interrupts:
  TRAP
  RST 5.5
  RST 6.5
  RST 7.5
  INTR
It provides accumulator, 5 flag register, 6 general purpose registers and 2 special purpose registers (SP,PC).

## Slide 8: 8085 Programming Model

## Slide 9: 8085 Programming Model
Accumulator A (8)
B (8)
D (8)
E (8)
C (8)
H (8)
L (8)
Stack Pointer (SP) (16)
Program Counter (PC) (16)
Address Bus
Data Bus
8
Bidirectional
16
Unidirectional
Flag Register
General Purpose Registers

## Slide 10: General Purpose Registers
6 general purpose registers to store 8-bit data B, C, D, E, H & L.
Can be combined as fixed register pairs – BC, DE, HL to perform 16 bit operations.
Used to store or copy data using data copy instructions.
B (8)
D (8)
E (8)
C (8)
H (8)
L (8)

## Slide 11: 8085 Programming Model
Accumulator A (8)
B (8)
D (8)
E (8)
C (8)
H (8)
L (8)
Stack Pointer (SP) (16)
Program Counter (PC) (16)
Address Bus
Data Bus
8
Bidirectional
16
Unidirectional
Flag Register

## Slide 12: Accumulator
8 - bit register, identified as A
Part of ALU
Used to store 8-bit data to perform arithmetic & logical operations.
Result of operation is stored in Accumulator.

## Slide 13: 8085 Programming Model
Accumulator A (8)
B (8)
D (8)
E (8)
C (8)
H (8)
L (8)
Stack Pointer (SP) (16)
Program Counter (PC) (16)
Address Bus
Data Bus
8
Bidirectional
16
Unidirectional
Flag Register

## Slide 14: Flag Register
S | Z |  | AC |  | P |  | CY
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
S -Sign Flag
Set (1) if 7th bit of result is 1;
otherwise reset (0)
Z -Zero Flag
Set (1) when result is zero; otherwise reset(0)
AC -Auxiliary Carry Flag
Set (1) when carry bit is generated by 3rd bit & passed to bit 4th bit.
P -Parity Flag
Set (1) if result has even no. of 1’s & Reset(0) if result has odd no. of 1’s
CY -Carry Flag
Set (1) if arithmetic operation results in carry;
otherwise reset(0)
1 1 1
0 0 1 0 1 0 1 0
+ 0 1 1 0 1 0 0 1
1 0 0 1 0 0 1 1
AC = 1
1 0 1 0 1 0 1 0
S = 1
1 0 1 0
- 1 0 1 0
0 0 0 0
Z = 1
1 0 0 1 0 0 1 1
P = 1
1 1 1
1 0 1 0 1 0 1 0
+ 0 1 1 0 1 0 0 1
1 0 0 0 1 0 0 1 1
CY = 1
:Undefined

## Slide 15: Flag Register
ALU has 5 Flag Register that set/reset after an operation according to data conditions of the result in accumulator & other registers.
Helpful in decision making process of microprocessor.
Conditions are tested through software instructions.
For e.g.
JC (Jump On Carry) is implemented to change the sequence of program when CY(Carry Flag) is set(1).

## Slide 16: 8085 Programming Model
Accumulator A (8)
B (8)
D (8)
E (8)
C (8)
H (8)
L (8)
Stack Pointer (SP) (16)
Program Counter (PC) (16)
Address Bus
Data Bus
8
Bidirectional
16
Unidirectional
Flag Register

## Slide 17: Stack Pointer & Program Counter
Stack Pointer(SP)
Used as memory pointer.
Points to the memory location in R/W memory, called Stack.
Beginning of stack is defined by loading a 16-bit address in the stack pointer.
Program Counter(PC)
Microprocessor uses PC register to sequence the execution of instructions.
Its function is to point to memory address from which next byte is to be fetched.
When a byte is being fetched, PC is incremented by 1 to point next memory location.
GTU Que: Explain 8085 Programming Model and flag register.[7m] (W’18,W’19)

## Slide 18: Bus Organization of 8085

## Slide 19: System bus
CPU
Memory
Input/Output
Control Bus
Address Bus
Data Bus
System Bus

## Slide 20: Bus Organization of 8085
8085 MPU
Address Bus
A0
A15
Control Bus
Memory
Input
Output
D0
D7
Data Bus

## Slide 21: Address bus
Group of 16 unidirectional lines generally identified as A0 to A15.
i.e. bits flow from microprocessor to peripheral devices.
16 address lines are capable of addressing 65536 memory locations. So, 8085 has 64K memory locations.

## Slide 22: Bus Organization of 8085
8085 MPU
Address Bus
A0
A15
Control Bus
Memory
Input
Output
Real World
D0
D7
Data Bus

## Slide 23: Data bus
Group of 8 lines identified as D0 to D7.
They are bidirectional i.e. data flow in both directions between microprocessor, memory & peripheral.
8 data lines enable microprocessor to manipulate data ranging from 00 H to FF H (28=256 numbers).
Largest number appear on data bus is 1111 1111 => (255)10.
As Data bus is of 8-bit, 8085 is known as 8-bit Microprocessor.
Notes: 8086- 16-nit
386,486-32 bit

## Slide 24: Bus Organization of 8085
8085 MPU
Address Bus
A0
A15
Control Bus
Memory
Input
Output
D0
D7
Data Bus

## Slide 25: Control bus
It comprises of various single lines that carry synchronization, timing & control signals.
These signals are used to identify a device type with which MPU intends to communicate.
Some control signals are Read, Write and Opcode fetch etc.

## Slide 26: 8085 pin diagram
8085 pin diagram

## Slide 27
8085 pin diagram
8-bit general purpose microprocessor.
Capable of addressing 64K of memory.
It has 40 pins.
Requires +5V single power supply.

## Slide 28: 8085 pin diagram
Signals are classified into 6 groups:
Address bus
Multiplexed address/data bus
Control & status signals
Power supply & frequency signals
Externally initiated signals
Serial I/O ports

## Slide 29: 8085 pin diagram: Address Bus
16 signal lines are used as address bus.
However these lines are split into two segments: A15 - A8 and AD7 - AD0
A15 - A8 are unidirectional and used to carry high-order address of 16-bit address.
AD7 - AD0 are used for dual purpose.

## Slide 30: 8085 pin diagram: Multiplexed Address/Data Bus
Signal lines AD7-AD0 are bidirectional and serve dual purpose.
They are used as low-order address bus as well as data bus.
The low-order address bus can be separate from these signals by using a latch (ALE).

## Slide 31: 8085 pin diagram: Control & Status Signals
To identify nature of operation
Two Control Signals
  RD(Read)
  WR(Write)
Three Status Signals
  S1
  S0
  IO/M
To indicate beginning of operation
  ALE(Address Latch Enable)
  ALE  1, then Address bus
  ALE  0, then Data bus

## Slide 32: 8085 pin diagram: Control & Status Signals
ALE: Pin 30
This is positive going pulse generated every time the 8085 begins an operation (machine cycle).
It indicates that the bits on AD7-AD0 are address bits.
This signal is used primarily to latch the low-address from multiplexed bus & generate a separate set of address lines A7-A0.

## Slide 33: 8085 pin diagram: Control & Status Signals
RD(Read): Pin 32
This is a read control signal (active low)
This signal indicates that the selected I/O or Memory device is to be read & data is available on data bus.

## Slide 34: 8085 pin diagram: Control & Status Signals
WR (Write): Pin 31
This is a write control signal (active low)
This signal indicates that the selected I/O or Memory device is to be write & data is available on data bus.

## Slide 35: 8085 pin diagram: Control & Status Signals
IO/M: Pin 34
This is a status signal used to differentiate I/O and memory operation.
When signal is
high  I/O operation
low  Memory operation
This signal is combined with RD and WR to generate I/O & memory control signals.

## Slide 36: 8085 pin diagram: Control & Status Signals
S1 (Pin 33) & S0 (Pin 29)
These status signals can identify various operations.
S1 | S0 | Mode
0 | 0 | HLT
0 | 1 | WRITE
1 | 1 | OPCODE FETCH
1 | 0 | READ

## Slide 37: 8085 pin diagram
I0/M | RD | WR | Operation
0 | 0 | 1 | 
MEMR
0 | 1 | 0 | 
MEMW
0 | 1 | 1 | Opcode Fetch
1 | 0 | 1 | 
IOR
1 | 1 | 0 | 
IOW
1 | 1 | 1 | NOP
0 | 0 | 0 | HLT
1 | 0 | 0 | HLT

## Slide 38: 8085 Pin Diagram: Power Supply & Frequency Signal
Vcc  Pin 40, +5V Supply.
Vss  Pin 20, Ground Reference

## Slide 39: 8085 Pin Diagram: Power Supply & Frequency Signal
X1, X2  Pin 1 & 2, Crystal Oscillator is connected at these two pins.
The frequency is internally divided by two;
therefore, to operate a system at 3MHz, the crystal should have a frequency of 6MHz.

## Slide 40: 8085 Pin Diagram: Power Supply & Frequency Signal
CLK (OUT)  Clock output
Pin 37: This signal is used as system clock for other I/O devices for synchronization with Microprocessor.

## Slide 41: 8085 Pin Diagram: Externally Initiated Signals
INTR(Input)  Interrupt Request
It is used for general purpose interrupt.
INTA(Output)  Interrupt Acknowledge.

## Slide 42: 8085 Pin Diagram: Externally Initiated Signals
RST7.5, RST6.5, RST5.5 (Input)  Restart Interrupts.
These are vector interrupts that transfer the program control to specific memory locations.
RST7.5, RST6.5, RST5.5 have higher priorities than INTR interrupt.
Among these 3 interrupts, the priority order (higher to lower) is RST7.5, RST6.5, RST5.5 respectively.
Notes: In a computer, a vectored interrupt is an I/O interrupt that tells the part of the computer that handles I/O interrupts at the hardware level that a request for attention from an I/O device has been received and also identifies the device that sent the request.

## Slide 43: 8085 Pin Diagram: Externally Initiated Signals
TRAP(Input)  This is a non maskable interrupt & has the highest priority.

## Slide 44: 8085 Pin Diagram: Externally Initiated Signals
HOLD(Input)  This signal indicates that a peripheral such as DMA Controller is requesting the use of address & data buses.
HLDA(Output)  Hold Acknowledge. This signal acknowledges the HOLD request.
Notes: Direct Memory Access Controller is an external device that controls the transfer of data between I/O device and memory without the involvement of the processor. It holds the ability to directly access the main memory for read or write operation.

## Slide 45: 8085 Pin Diagram: Externally Initiated Signals
READY(Input)  This signal is used to delay the microprocessor read or write cycles until low-responding peripheral is ready to send or accept data.
When the signal goes low, the microprocessor waits for an integral no. of clock cycles until READY signal goes high.

## Slide 46: 8085 Pin Diagram: Externally Initiated Signals
RESET IN (Input)  When the signal on this pin goes low, the Program Counter is set to zero, the buses are tri-stated & microprocessor is reset.
RESET OUT (Output)  This signal indicates that microprocessor is being reset. The signal is also used to reset other devices.

## Slide 47: 8085 Pin Diagram: Serial I/O Ports
Two pins for serial transmission
  SID (Serial Input Data)
  SOD (Serial Output Data)
In serial transmission, data bits are sent over a single line, one bit at a time.

## Slide 48
X1 |  | 1 | 8085A | 40 |  | VCC
X2 |  | 2 |  | 39 |  | HOLD
RESET OUT |  | 3 |  | 38 |  | HLDA
SOD |  | 4 |  | 37 |  | CLK (OUT)
SID |  | 5 |  | 36 |  | RESET IN
TRAP |  | 6 |  | 35 |  | READY
RST7.5 |  | 7 |  | 34 |  | IO/M
RST6.5 |  | 8 |  | 33 |  | S1
RST5.5 |  | 9 |  | 32 |  | RD
INTR |  | 10 |  | 31 |  | WR
INTA |  | 11 |  | 30 |  | ALE
AD0 |  | 12 |  | 29 |  | S0
AD1 |  | 13 |  | 28 |  | A15
AD2 |  | 14 |  | 27 |  | A14
AD3 |  | 15 |  | 26 |  | A13
AD4 |  | 16 |  | 25 |  | A12
AD5 |  | 17 |  | 24 |  | A11
AD6 |  | 18 |  | 23 |  | A10
AD7 |  | 19 |  | 22 |  | A9
VSS |  | 20 |  | 21 |  | A8
Sr. | GTU Questions | Marks | Year
1. | Draw and Explain the pin diagram of 8085 microprocessor. | 7 | Win-2019
2. | What is the use of ALE pin in 8085? | 1 | Sum-2019
3. | Explain the following pins of the 8085 microprocessor: IO/M , INTR, RESETIN | 3 | Win-2017

## Slide 49
8085A
1
2
40
20
+5 V
GND
SID
SOD
5
4
Serial I/O Ports
High-Order Address Bus
21
28
TRAP
RST 7.5
6
7
RST 6.5
RST 5.5
8
9
INTR
10
READY
HOLD
35
39
RESET IN
36
INTA
HLDA
11
38
Externally Initiated Signals
External Signal Acknowledgement
Multiplexed Address/Data Bus
19
12
ALE
30
29
IO/M
33
32
34
31
RD
WR
37
3
CLK OUT
RESET OUT
Control and Status Signals
8085 Microprocessor signals

## Slide 50: 8085 Architecture/Block Diagram

## Slide 51
INTA
B (8)
Reg.
C (8)
Reg.
D (8)
Reg.
E (8)
Reg.
H (8)
Reg.
L (8)
Reg.
Accumulator (8)
W (8)
Temp. Reg.
Z (8)
Temp. Reg.
Stack Pointer (16)
Program Counter (16)
Increment/Decrement Address Latch (16)
Register Select
Multiplexer
Arithmetic Logic Unit (ALU) (8)
Flag (5) Flip-Flops
Temp. Reg. (8)
Instruction Reg. (8)
Instruction Decoder and Machine Cycle Encoding
Address Buffer (8)
Data/Address Buffer (8)
A15 - A8 Address Bus
AD7 – AD0 Address/Data Bus
Interrupt Control
INTR
RST5.5
TRAP
RST7.5
RST6.5
Serial I/O Control
SID
SOD
Timing and Control
X1
X2
CLK GEN
CLK OUT
READY
WR
RD
ALE
HOLD
HLDA
RESET IN
RESET OUT
S0
S1
Control
Status
DMA
Reset
Power Supply
+5 V
8-Bit Internal Data Bus
GND
IO/M
8085 Block Diagram

## Slide 52
INTA
B (8)
Reg.
C (8)
Reg.
D (8)
Reg.
E (8)
Reg.
H (8)
Reg.
L (8)
Reg.
Accumulator (8)
W (8)
Temp. Reg.
Z (8)
Temp. Reg.
Stack Pointer (16)
Program Counter (16)
Increment/Decrement Address Latch (16)
Register Select
Multiplexer
Arithmetic Logic Unit (ALU) (8)
Flag (5) Flip-Flops
Temp. Reg. (8)
Instruction Reg. (8)
Instruction Decoder and Machine Cycle Encoding
Address Buffer (8)
Data/Address Buffer (8)
A15 - A8 Address Bus
AD7 – AD0 Address/Data Bus
Interrupt Control
INTR
RST5.5
TRAP
RST7.5
RST6.5
Serial I/O Control
SID
SOD
Timing and Control
X1
CLK GEN
CLK OUT
READY
WR
RD
ALE
HOLD
HLDA
RESET IN
RESET OUT
S0
S1
Control
Status
DMA
Reset
8-Bit Internal Data Bus
Used to store 8-bit data to perform arithmetic & logical operations.
Result of operation is stored in Accumulator.
Used to hold data (i.e. temporary data) during ALU operation.
S | Z |  | AC |  | P |  | CY
When Instruction is fetched from memory, it is loaded in the Instruction Registor (IR).
Instruction decoder decodes the information present in the Instruction register.
Performs Computing Functions.
Accumulator, Temporary Register and Flag Registers are part of ALU.

## Slide 53
INTA
B (8)
Reg.
C (8)
Reg.
D (8)
Reg.
E (8)
Reg.
H (8)
Reg.
L (8)
Reg.
Accumulator (8)
W (8)
Temp. Reg.
Z (8)
Temp. Reg.
Stack Pointer (16)
Program Counter (16)
Increment/Decrement Address Latch (16)
Register Select
Multiplexer
Arithmetic Logic Unit (ALU) (8)
Flag (5) Flip-Flops
Temp. Reg. (8)
Instruction Reg. (8)
Instruction Decoder and Machine Cycle Encoding
Address Buffer (8)
Data/Address Buffer (8)
A15 - A8 Address Bus
AD7 – AD0 Address/Data Bus
Interrupt Control
INTR
RST5.5
TRAP
RST7.5
RST6.5
Serial I/O Control
SID
SOD
Timing and Control
X1
CLK GEN
CLK OUT
READY
WR
RD
ALE
HOLD
HLDA
RESET IN
RESET OUT
S0
S1
Control
Status
DMA
Reset
8-Bit Internal Data Bus
Each register can hold 8-bit data.
These registers can work in pair to hold 16-bit data and their pairing combination is like B-C, D-E & H-L.
Two additional 8-bit register, which holds the temporary data during execution of some instructions.
They are used internally, so they are not available to the programmer.
It is a 16-bit register works like stack, which is always incremented/decremented by 2 during push & pop operations.
16-bit register used to store the memory address location of the next instruction to be executed.
A multiplexer pulls out the right group of bits, depending on the instruction.
It increments the program counter as instructions execute, increments and decrements the stack pointer as needed, and supports the 16-bit increment and decrement instructions.
The content stored in the SP and PC is loaded into the Address Buffer and Data/Address Buffer.
The memory and I/O chips are connected to these buses that can exchange the data.

## Slide 54
X2
INTA
B (8)
Reg.
C (8)
Reg.
D (8)
Reg.
E (8)
Reg.
H (8)
Reg.
L (8)
Reg.
Accumulator (8)
W (8)
Temp. Reg.
Z (8)
Temp. Reg.
Stack Pointer (16)
Program Counter (16)
Increment/Decrement Address Latch (16)
Register Select
Multiplexer
Arithmetic Logic Unit (ALU) (8)
Flag (5) Flip-Flops
Temp. Reg. (8)
Instruction Reg. (8)
Instruction Decoder and Machine Cycle Encoding
Address Buffer (8)
Data/Address Buffer (8)
A15 - A8 Address Bus
AD7 – AD0 Address/Data Bus
Interrupt Control
INTR
RST5.5
TRAP
RST7.5
RST6.5
Serial I/O Control
SID
SOD
Timing and Control
X1
CLK GEN
CLK OUT
READY
WR
RD
ALE
HOLD
HLDA
RESET IN
RESET OUT
S0
S1
Control
Status
DMA
Reset
8-Bit Internal Data Bus
This unit synchronizes all the microprocessor operations with the clock and generates control signal necessary for communication between microprocessor & peripheral.
Frequency Control Signals
Perform synchronization with peripheral device.
Input signal to synchronize microprocessor with peripheral device.
Read/write either to/from memory or peripherals.
Address Latch Enable control signal
Shows read/write status to/from memory or I/O.
DMA control signal
Signal to RESET microprocessor and other devices connected to it.

## Slide 55
X2
INTA
B (8)
Reg.
C (8)
Reg.
D (8)
Reg.
E (8)
Reg.
H (8)
Reg.
L (8)
Reg.
Accumulator (8)
W (8)
Temp. Reg.
Z (8)
Temp. Reg.
Stack Pointer (16)
Program Counter (16)
Increment/Decrement Address Latch (16)
Register Select
Multiplexer
Arithmetic Logic Unit (ALU) (8)
Flag (5) Flip-Flops
Temp. Reg. (8)
Instruction Reg. (8)
Instruction Decoder and Machine Cycle Encoding
Address Buffer (8)
Data/Address Buffer (8)
A15 - A8 Address Bus
AD7 – AD0 Address/Data Bus
Interrupt Control
INTR
RST5.5
TRAP
RST7.5
RST6.5
Serial I/O Control
SID
SOD
Timing and Control
X1
CLK GEN
CLK OUT
READY
WR
RD
ALE
HOLD
HLDA
RESET IN
RESET OUT
S0
S1
Control
Status
DMA
Reset
8-Bit Internal Data Bus

## Slide 56
X2
INTA
B (8)
Reg.
C (8)
Reg.
D (8)
Reg.
E (8)
Reg.
H (8)
Reg.
L (8)
Reg.
Accumulator (8)
W (8)
Temp. Reg.
Z (8)
Temp. Reg.
Stack Pointer (16)
Program Counter (16)
Increment/Decrement Address Latch (16)
Register Select
Multiplexer
Arithmetic Logic Unit (ALU) (8)
Flag (5) Flip-Flops
Temp. Reg. (8)
Instruction Reg. (8)
Instruction Decoder and Machine Cycle Encoding
Address Buffer (8)
Data/Address Buffer (8)
A15 - A8 Address Bus
AD7 – AD0 Address/Data Bus
Interrupt Control
INTR
RST5.5
TRAP
RST7.5
RST6.5
Serial I/O Control
SID
SOD
Timing and Control
X1
CLK GEN
CLK OUT
READY
WR
RD
ALE
HOLD
HLDA
RESET IN
RESET OUT
S0
S1
Control
Status
DMA
Reset
8-Bit Internal Data Bus
%
It controls the interrupts during a process.
There are 5 interrupt signals in 8085 microprocessor:
TRAP, RST 7.5, RST 6.5, RST 5.5, INTR.
It controls the serial data communication by using two instructions:
SID (Serial input data)
SOD (Serial output data)

## Slide 57
AD7 – AD0 Address/Data Bus
INTA
B (8)
Reg.
C (8)
Reg.
D (8)
Reg.
E (8)
Reg.
H (8)
Reg.
L (8)
Reg.
Accumulator (8)
W (8)
Temp. Reg.
Z (8)
Temp. Reg.
Stack Pointer (16)
Program Counter (16)
Increment/Decrement Address Latch (16)
Register Select
Multiplexer
Arithmetic Logic Unit (ALU) (8)
Flag (5) Flip-Flops
Temp. Reg. (8)
Instruction Reg. (8)
Instruction Decoder and Machine Cycle Encoding
Address Buffer (8)
Data/Address Buffer (8)
A15 - A8 Address Bus
Interrupt Control
INTR
RST5.5
TRAP
RST7.5
RST6.5
Serial I/O Control
SID
SOD
Timing and Control
X1
X2
CLK GEN
CLK OUT
READY
WR
RD
ALE
HOLD
HLDA
RESET IN
RESET OUT
S0
S1
Control
Status
DMA
Reset
Power Supply
+5 V
8-Bit Internal Data Bus
GND

## Slide 58: GTU Exam Questions
Sr. | GTU Questions | Marks | Year
1. | Draw and explain the internal block diagram of 8085 microprocessor. | 7 | Sum-2019 Win-2018 Sum-2018

## Slide 59: T-States, Machine and Instruction Cycle

## Slide 60: T-States, Machine and Instruction Cycle
Instruction Cycle
Machine Cycle
T-States
Time required to complete execution of an instruction.
Time required by the microprocessor to complete an operation.
Operation performed in one clock period.

## Slide 61: T-States
“T-States are defined as operation performed in one clock period.”
These sub-divisions are internal states synchronized with system clock & each T-state is precisely equal to one clock period.
 | T-State-1 | T-State-2 | T-State-3 | T-State-4
CLK
Clock Period

## Slide 62: Machine Cycle
“Machine Cycle is defined as time required by the microprocessor to complete an operation.“
This cycle may consist 3 to 6 T-states.
The basic microprocessor operation such as reading a byte from I/O port or writing a byte to memory.
 | T1 | T2 | T3 | T4 | T1 | T2 | T3 | T1 | T2 | T3
Opcode Fetch
Memory Read
CLK
I/O Write
Machine Cycle-1
Machine Cycle-2
Machine Cycle-3
m/m Read
Fetch
IO write

## Slide 63: Instruction Cycle
“Instruction Cycle is defined as time required to complete execution of an instruction.”
In 8085 microprocessor instruction cycle consists of 1 to 6 Machine Cycles or 1 to 6 operations.
 | T1 | T2 | T3 | T4
CLK
Instruction Cycle
Fetch Cycle
Execute Cycle

## Slide 64
 | T-State-1 | T-State-2 | T-State-3 | T-State-4
CLK
Clock Period
 | T1 | T2 | T3 | T4 | T1 | T2 | T3 | T1 | T2 | T3
Opcode Fetch
Memory Read
CLK
I/O Write
Machine Cycle-1
Machine Cycle-2
Machine Cycle-3
 | T1 | T2 | T3 | T4
CLK
Instruction Cycle
Fetch Cycle
Execute Cycle
Instruction Cycle
Machine Cycle
T-States

## Slide 65
Instruction Cycle
Machine Cycle
T-States

## Slide 66: Demultiplexing Address and Data Bus AD0-AD7

## Slide 67
A15
A15
0
A14
0
A13
1
A12
0
A11
0
A10
0
A9
0
A8
0
G
Enable
A7
A6
A5
A4
A3
A2
A1
A0
0
0
0
0
1
0
1
1
D6
D5
D4
D3
D2
D1
D0
D7
0
0
0
1
1
1
1
1
High-Order Address Bus
Low-Order Address Bus
Data Bus
A8
ALE
AD7
AD0
Demultiplexing AD0-AD7
ALE=1
Address Bus
ALE= 0
Data Bus
8085 Microprocessor

## Slide 68: Demultiplexing AD0-AD7
The dual-purpose of the AD0-AD7 pins is achieved through multiplexing.
In simple words, multiplexing allows us to use the pins of a microprocessor for more than one function.
Advantage: Since each pin can serve multiple purposes, the total number of pins can be reduced.
IC 74LS373
IC 74LS373 is an IC with 20 pins.
it is a memory unit to hold one bit of data.
IC 74LS373

## Slide 69: GTU Questions
Sr. | GTU Questions | Marks | Year
1. | How will the multiplexed address/data bus (AD0-AD7) of the 8085 microprocessor be demultiplexed? | 4 | Win-2017

## Slide 70: Timing Diagram

## Slide 71: Timing Diagram

## Slide 72
 | T1 | T2 | T3 | T4
High order memory address
Unspecified
Low order M/m addr.
Opcode
CLK
A8
AD0
AD7
ALE
IO/M
RD
A15
Opcode Fetch
Timing Diagram: Opcode Fetch

## Slide 73
 | T1 | T2 | T3 | T4
High order memory address
Low order M/m addr.
Data from memory
CLK
A8
AD0
AD7
ALE
IO/M
RD
A15
Memory read cycle
S1 | S0 | Mode
0 | 0 | HLT
0 | 1 | WRITE
1 | 0 | READ
IO/M=0, S1=1 , S0=0
S1
S0
Timing Diagram: Memory Read Cycle

## Slide 74
 | T1 | T2 | T3 | T4
High order memory address
Low order M/m addr.
Data from Microprocessor
CLK
A8
AD0
AD7
ALE
IO/M
WR
A15
Memory write cycle
S1 | S0 | Mode
0 | 0 | HLT
0 | 1 | WRITE
1 | 0 | READ
IO/M=0, S0=1 , S1=0
S0
S1
Timing Diagram: Memory Write Cycle

## Slide 75: Memory Interfacing

## Slide 76: Memory structure
N X M
Memory
Input Buffer
Output Buffer
Internal Decoder
Data Inputs
A0
A10
Address
Input
Data Output
WR
CS
RD
Block diagram of Memory Device: RAM
N=Number of Register
M=Word Length
E.g.
If a memory is having
address lines=13
data lines=8
then
Number of memory locations = N=213 = 8192
Word length M= 8 bit
Therefore, N X M= 8192 X 8

## Slide 77: Memory structure
No. of Lines | Memory size(bytes)
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256
No. of Lines | Memory size(bytes)
9 | 512
10 | 1024=1k
11 | 2048=2k
12 | 4096=4k
13 | 8192=8k
14 | 16384=16k
15 | 32768=32k
16 | 65536=64k

## Slide 78: Memory Interfacing
8085 can access 64K of memory, thus address bus is of 16-bit.
It is not always necessary to use full 64K address space. The total memory size depends upon the application.
Generally EPROM is used as a program memory and RAM is used as data memory.
When both are used then total 64K address will be shared by both.
The capacity of program memory and data memory depends on the application.

## Slide 79: Memory Interfacing
It is not always necessary to select 1 EPROM and 1 RAM. We can have multiple EPROMs and multiple RAMs as per the requirement of application.
We can place EPROM / RAM anywhere in full 64 Kbytes address space.
Program memory (EPROM) should be located from address 0000H, since reset address of 8085 microprocessor is 0000H.
It is not always necessary to locate EPROM and RAM in consecutive memory addresses.

## Slide 80: Memory Interfacing: Example 1
Interface 4kB of EPROM with starting address from 0000H and 2kB of RAM with starting address followed by EPROM
Step-1: To calculate no. of EPROM and RAM chip required
Total EPROM required = 4kB
Chip size available = 4kB
No. of chips required = 4kB/4kB=1
Total RAM required = 2kB
Chip Size Available = 2kB
No. of Chips required = 2kB/2kB=1

## Slide 81: Memory Interfacing: Example 1
Step-2: To calculate starting and ending address of EPROM
EPROM Chip-1:
Starting Address = 0000H
Chip Size = 4kB (i.e. address Line=12, m/m = 212 = 4096B = 4k)
Ending Address = 0FFFH
Step-3: To calculate starting and ending address of RAM
RAM Chip-1:
Starting address = Ending address of EPROM +1
= 0FFFH+1
= 1000H
Chip Size = 2kB = 07FFH
Ending address = 1000H+07FFH
= 17FFH

## Slide 82: Memory Interfacing: Example 1
Step-4: Memory Map | A 15 | A 14 | A 13 | A 12 | A 11 | A 10 | A 9 | A 8 | A 7 | A 6 | A 5 | A 4 | A 3 | A 2 | A 1 | A 0
EPROM 4k | Start Address 0000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 0FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
RAM 2k | Start Address 1000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 17FF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
1
1
1
1
1
1
1
1
1
1
1
0
1
0
0
0
EPROM chip size = 4kB & RAM chip size = 2kB
smaller chip size RAM = 2kB = 211
Thus neglect lower 11 address lines (A0 to A10), and consider A11 to A15 for Decoding.

## Slide 83: Memory Interfacing: Example 1
 |  | A 15 | A 14 | A 13 | A 12 | A 11 | A 10 | A 9 | A 8 | A 7 | A 6 | A 5 | A 4 | A 3 | A 2 | A 1 | A 0
EPROM | Start Address 0000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 0FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
EPROM
Required Address Lines: A11 to A15.
Now, EPROM has two Possibilities, either 00000 b or 00001 b.
Therefore, it requires Y0 and Y1 outputs of decoder.

## Slide 84: Memory Interfacing: Example 1
 |  | A 15 | A 14 | A 13 | A 12 | A 11 | A 10 | A 9 | A 8 | A 7 | A 6 | A 5 | A 4 | A 3 | A 2 | A 1 | A 0
EPROM | Start Address 0000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 0FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
RAM | Start Address 1000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 17FF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
1
1
1
1
1
1
1
1
1
1
1
0
1
0
0
0
RAM has 00010 b, hence it requires Y2 output of decoder.

## Slide 85
EPROM
RAM
D0
-
D7
A0 - A10
D0 – D7
A0 - A10
Memory Interfacing: Example 1 Implementation
Step-5:
5:32
Decoder
A11
A12
A13
A14
A15
Y0
Y1
Y2
To EPROM
To RAM
IO/M
RD
OE
WR
OE
RD
00010
00000
00001

## Slide 86: Memory Interfacing: Example 2
Interface 16kB of EPROM with chip size of 8kB and starting address from 0000H and 8kB of RAM with starting address followed by EPROM.
Step-1: To calculate no. of EPROM and RAM chip required
Total EPROM required =16kB
Chip size available = 8kB
No. of chips required = 16kB/8kB = 2
Total RAM required = 8kB
Chip size available = 8kB
No. of chips required = 8kB/8kB = 1

## Slide 87: Memory Interfacing: Example 2
Step-2: To calculate starting and ending address of EPROM
EPROM Chip-1:
Starting Address = 0000H
Chip Size = 8kB (i.e. address Line=13, m/m=213 =8192B =8k)
Ending Address = 1FFFH
EPROM Chip-2:
Starting Address =1FFFH + 1 = 2000H
Chip Size = 1FFFH
Ending Address = 2000+1FFFH = 3FFFH

## Slide 88: Memory Interfacing: Example 2
Step-3: RAM Chip-1:
Starting Address = EPROM ending address + 1
Starting Address = 3FFFH+1 = 4000H
Chip Size = 8kB (i.e. address Line =13, m/m=213 = 8192B =8k)
Chip Size = 1FFFH
Ending Address = 4000h+1FFFH = 5FFFH

## Slide 89: Memory Interfacing: Example 2
Step-4: Memory Map | A 15 | A 14 | A 13 | A 12 | A 11 | A 10 | A 9 | A 8 | A 7 | A 6 | A 5 | A 4 | A 3 | A 2 | A 1 | A 0
EPROM1 | Start Address 0000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 1FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
EPROM2 | Start Address 2000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 3FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
RAM | Start Address 4000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 5FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
0

## Slide 90: Memory Interfacing: Example 2
Step-5:Interface Implementation
EPROM chip size = RAM chip size = 8kB = 213
Therefore, neglect lower 13 address lines (i.e. A0 to A12) and consider only A13 to A15 for decoding.
EPROM CHIP-01 | 000
EPROM CHIP-02 | 001
RAM CHIP-01 | 010
3:8
Decoder
A13
A14
A15
Y0
Y1
Y2
To EPROM Chip-1
To RAM Chip-1
To EPROM Chip-2
Y7

## Slide 91: Memory Interfacing: Example 2
Step-4: Memory Map | A 15 | A 14 | A 13 | A 12 | A 11 | A 10 | A 9 | A 8 | A 7 | A 6 | A 5 | A 4 | A 3 | A 2 | A 1 | A 0
EPROM1 | Start Address 0000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 1FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
EPROM2 | Start Address 2000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 3FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
RAM | Start Address 4000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 5FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
0

## Slide 92
Memory Interfacing: Example 2 Implementation
Step-5:
EPROM
CHIP-1
RAM
D0
-
D7
A0 - A12
D0 – D7
A0 - A12
3:8
Decoder
A13
A14
A15
Y0
Y1
Y2
To EPROM CHIP-1
To RAM
IO/M
RD
OE
WR
OE
RD
010
000
001
EPROM
CHIP-2
D0 – D7
A0 - A12
OE
To EPROM CHIP-2

## Slide 93: Exercise: Memory Interface Example
Draw the interfacing of a 4KB EPROM having a starting address 2000h and two 2KB static RAMs having starting addresses 4000h and 8000h, respectively, with 8085 microprocessor.
Design an 8085 microprocessor system such that it should contain 16KB of EPROM and 4KB of RAM with starting addresses 0000H and 4000H respectively. Use two 8KB of EPROMs (2764) and two 2KB of RAMs (6116) for this system.

## Slide 94: Exercise: Example 1
Step-4: Memory Map | A 15 | A 14 | A 13 | A 12 | A 11 | A 10 | A 9 | A 8 | A 7 | A 6 | A 5 | A 4 | A 3 | A 2 | A 1 | A 0
EPROM1 | Start Address 2000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 2FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
0
1
0
0
RAM 1 | Start Address 4000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 47FF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
1
1
1
1
0
0
0
1
0
RAM 2 | Start Address 8000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 87FF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1

## Slide 95
Exercise: Example 1
Step-5:
EPROM
CHIP
RAM-2
D0
-
D7
A0 - A12
D0 – D7
A0 - A12
5:32
Decoder
A13
A14
A15
IO/M
RD
OE
WR
OE
RD
RAM-1
D0 – D7
A0 - A12
OE
A12
A11
Y0
Y1
Y2
To EPROM
To RAM-1
01000
00100
00101
Y3
To RAM-2
10000

## Slide 96
Step-4: Memory Map | A 15 | A 14 | A 13 | A 12 | A 11 | A 10 | A 9 | A 8 | A 7 | A 6 | A 5 | A 4 | A 3 | A 2 | A 1 | A 0
EPROM1 | Start Address 0000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 1FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
EPROM2 | Start Address 2000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 3FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
RAM 1 | Start Address 4000 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 47FF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
1
1
1
1
0
0
0
1
0
Exercise: Example 2
RAM 2 | Start Address 4800 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | End Address 4FFF H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 97
Exercise: Example 2
Step-5:
EPROM-1
RAM-2
D0
-
D7
A0 - A10
D0 – D7
A0 - A10
5:32
Decoder
A13
A14
A15
IO/M
RD
OE
WR
OE
RD
RAM-1
D0 – D7
A0 - A10
OE
A12
A11
Y0
Y1
Y3
EPROM-1
To RAM-1
01000
00100
00011
Y4
To RAM-2
10000
Y2
EPROM-2
00101
EPROM-2
D0
-
D7
A0 - A10
OE

## Slide 98: Generating Control Signals

## Slide 99: Generating Control Signals
8085
IO/M
RD
WR
MEMR
I0/M | RD | WR | Operation
0
0 | 0 | 0 | Invalid
0
1
0 | 0 | 1 | MEMR

## Slide 100: Generating Control Signals
8085
IO/M
RD
WR
MEMW
MEMR
I0/M | RD | WR | Operation
0
0 | 0 | 0 | Invalid
0 | 0 | 1 | 
MEMR
1
0
0 | 1 | 0 | 
MEMW
MEMR

## Slide 101: Generating Control Signals
8085
IO/M
RD
WR
MEMW
MEMR
I0/M | RD | WR | Operation
0
0 | 0 | 0 | Invalid
0 | 0 | 1 | 
MEMR
1
1
0 | 1 | 0 | 
MEMW
0 | 1 | 1 | NOP

## Slide 102: Generating Control Signals
8085
IO/M
RD
WR
MEMW
MEMR
I0/M | RD | WR | Operation
1
0 | 0 | 1 | 
MEMR
0
0
0 | 1 | 0 | 
MEMW
0 | 1 | 1 | NOP
1 | 0 | 0 | Invalid

## Slide 103: Generating Control Signals
8085
IO/M
RD
WR
IOR
MEMW
MEMR
I0/M | RD | WR | Operation
1
0 | 0 | 1 | 
MEMR
0
1
0 | 1 | 0 | 
MEMW
0 | 1 | 1 | NOP
1 | 0 | 1 | 
IOR

## Slide 104: Generating Control Signals
8085
IO/M
RD
WR
IOW
IOR
MEMW
MEMR
I0/M | RD | WR | Operation
1
0 | 0 | 1 | 
MEMR
1
0
0 | 1 | 0 | 
MEMW
0 | 1 | 1 | NOP
1 | 0 | 1 | 
IOR
1 | 1 | 0 | 
IOW

## Slide 105: Generating Control Signals
8085
IO/M
RD
WR
IOW
IOR
MEMW
MEMR
I0/M | RD | WR | Operation
1
0 | 0 | 1 | 
MEMR
1
1
0 | 1 | 0 | 
MEMW
0 | 1 | 1 | NOP
1 | 0 | 1 | 
IOR
1 | 1 | 0 | 
IOW
1 | 1 | 1 | NOP

## Slide 106: Generating Control Signals
I0/M | RD | WR | Operation
0 | 0 | 1 | 
MEMR
0 | 1 | 0 | 
MEMW
0 | 1 | 1 | NOP
1 | 0 | 1 | 
IOR
1 | 1 | 0 | 
IOW
1 | 1 | 1 | NOP
0 | 0 | 0 | HLT
1 | 0 | 0 | HLT

## Slide 107: GTU Exam Questions
Sr. | GTU Questions
1. | How will the multiplexed address/data bus (AD0-AD7) of the 8085 microprocessor be demultiplexed?
2. | Explain the flag register of the 8085 microprocessor with examples.
3. | Draw the interfacing of a 4KB EPROM having a starting address 2000h and two 2KB static RAMs having starting addresses 4000h and 8000h, respectively, with 8085 microprocessor. Use demultiplexed address/data lines and use 3-to-8 decoder (74LS138).
4. | Draw and explain the internal block diagram of 8085 microprocessor.
5. | List the sequence of events that occurs when the 8085 MPU reads from memory.
6. | Explain 8085 Programming Model and Flag Register.
7. | Discuss the programming model of 8085 μP with the help of suitable diagram.
8. | Draw and Explain the pin diagram of 8085 microprocessor.

## Slide 108: References
Book: | Microprocessor Architecture, Programming, and Applications with the 8085, Ramesh S. Gaonkar Pub: Penram International

## Slide 109: Thank You